## Slide 1: Overview
Last lecture
  "Switching-network" logic blocks
    Multiplexers/selectors
    Demultiplexers/decoders
  Programmable logic devices (PLDs)
    Regular structures for 2-level logic
Today
  PLDs
    PLAs
    PALs
  ROMs
  Tristates
  Design examples

## Slide 2: Programmable logic (PLAs & PALs )
• • •
• • •
inputs
outputs
product terms
AND array
OR array
Concept: Large array of uncommitted AND/OR gates
  Actually NAND/NOR gates
  You program the array by making or breaking connections
    Programmable block for sum-of-products logic

## Slide 3: Programming the wire connections
  Fuse: Comes connected; break unwanted connections
  Anti-fuse: Comes disconnected; make wanted connections
A
B
C
F1
F2
F3
F0
AB
B'C
AC'
B'C'
A
  F0 = A + B'C'
  F1 = AC' + AB
  F2 = B'C' + AB
  F3 = B'C + A
1

## Slide 4: Short-hand notation
  Draw multiple wires as a single wire or bus
  × signifies a connection
After Programming
F0
F1
AB
A'B'
CD'
C'D
A
B
C
D
Before Programming
F0 = AB + A'B'
F1 = CD' + C'D

## Slide 5: PLA example
A B C F1 F2 F3 F4 F5 F6
0 0 0 0 0 1 1 0 0
0 0 1 0 1 0 1 1 1
0 1 0 0 1 0 1 1 1
0 1 1 0 1 0 1 0 0
1 0 0 0 1 0 1 1 1
1 0 1 0 1 0 1 0 0
1 1 0 0 1 0 1 0 0
1 1 1 1 1 0 0 1 1
A'B'C'
A'B'C
A'BC'
A'BC
AB'C'
AB'C
ABC'
ABC
A
B
C
F1
F2
F3
F4
F5
F6
Think of as a memory-address decoder
Memory bits
  F1 = ABC
  F2 = A + B + C
  F3 = A' B' C'
  F4 = A' + B' + C'
  F5 = A xor B xor C
  F6 = A xnor B xnor C

## Slide 6: PLAs versus PALs
We've been looking at PLAs
  Fully programmable AND / OR arrays
    Can share AND terms
Programmable array logic (PAL)
  Programmable AND array
  OR array is prewired
    No sharing ANDs
    Cheaper and faster than PLAs

## Slide 7: Example: BCD to Gray code converter
00 0 0 X 1 01 0 1 X 1 11 0 1 X X 10 0 1 X X
00 0 1 X 0 01 0 1 X 0 11 0 0 X X 10 0 0 X X
00 0 0 X 1 01 1 0 X 0 11 0 1 X X 10 1 0 X X
A B C D W X Y Z 0 0 0 0 0 0 0 0 0 0 0 1 0 0 0 1 0 0 1 0 0 0 1 1 0 0 1 1 0 0 1 0 0 1 0 0 0 1 1 0 0 1 0 1 1 1 1 0 0 1 1 0 1 0 1 0 0 1 1 1 1 0 1 1 1 0 0 0 1 0 0 1 1 0 0 1 1 0 0 0 1 0 1 0 X X X X 1 0 1 1 X X X X
1 1 0 0 X X X X
1 1 0 1 X X X X
1 1 1 0 X X X X
1 1 1 1 X X X X
A
D
AB
CD
00
01
11
10
C
B
K-map for W
A
D
AB
CD
00
01
11
10
C
B
A
D
00 0 1 X 0 01 0 1 X 0 11 1 1 X X 10 1 1 X X
AB
CD
00
01
11
10
C
B
A
D
AB
CD
00
01
11
10
C
B
K-map for X
K-map for Y
K-map for Z

## Slide 8: Example (con’t): Wire a PLA
A B C D
W X Y Z
Minimized functions:
W = A + BC + BD
X = BC'
Y = B + C
Z = A'B'C'D + BCD
+ AD' + B'CD'

## Slide 9: Example: Wire a PAL
Minimized functions:
W = A + BC + BD
X = BC'
Y = B + C
Z = A'B'C'D + BCD
+ AD' + B'CD’
What do we do with the
unused AND gates?

## Slide 10: Compare implementations
PLA:
  No shared logic terms in this example
  10 decoded functions (10 AND gates)
PAL:
  Z requires 4 product terms
    16 decoded functions (16 AND gates)
    6 unused AND gates
This decoder is a poor candidate for PLAs/PALs
  10 of 16 possible inputs are decoded
  No sharing among AND terms
Better option?
  Yes — a ROM

## Slide 11: Read-only memories (ROMs)
Two dimensional array of stored 1s and 0s
  Input is an address  ROM decodes all possible input addresses
  Stored row entry is called a "word"
  ROM output is the decoded word
inputs
outputs
n address lines
2n word lines
decoder
• • •
• • •
memory array (2n words by m bits)

## Slide 12: ROM details
  Similar to a PLA but with a fully decoded AND array
  Completely flexible OR array (unlike a PAL)
  Extremely dense: One transistor per stored bit
decoder
0 n-1
Address
2
n-1
0
+5V
Bit lines: Normally pulled high through resistor. If transistor stores a zero, then
line pulls low when row is selected
1
2
Only one word line
is active at any time
0 m-1
Outputs

## Slide 13: Two-level combinational logic using a ROM
A B C F0 F1 F2 F3
0 0 0 0 0 1 0 0 0 1 1 1 1 0 0 1 0 0 1 0 0 0 1 1 0 0 0 1
1 0 0 1 0 1 1
1 0 1 1 0 0 0
1 1 0 0 0 0 1
1 1 1 0 1 0 0
ROM 8 words x 4 bits/word
address
outputs
A B C F0 F1 F2 F3
Use a ROM to directly store a truth table
  No need to minimize logic
  Example: F0 = A'B'C + AB'C' + AB'C
  F1 = A'B'C + A'BC' + ABC
  F2 = A'B'C' + A'B'C + AB'C'
  F3 = A'BC + AB'C' + ABC'
You specify whether to store 1 or 0 in each location in the ROM

## Slide 14: ROMs versus PLAs/PALs
ROMs
  Benefits
    Quick to design, simple, dense
  Limitations
    Size doubles for each additional input
    Can't exploit don't cares
PLAs/PALs
  Benefits
    Logic minimization reduces size
  Limitations
    PAL OR-plane has hard-wired fan-in
Another answer: Field programmable gate arrays
  Learn about in 467

## Slide 15: Loose end: Tristates
Tristate buffers have a control input
  Enabled: Buffer works normally
  Disabled: Buffer output is disconnected
OUT
In1
In2
Sel
2:1 Tristate Mux
module muxtri (In1,In2,Sel,OUT);
input In1,In2,Sel;
output OUT;
tri OUT;
bufif1 (OUT,In1,Sel);
bufif0 (OUT,In2,Sel);
endmodule

## Slide 16: Example: BCD to 7-segment display controller
BCD to 7–segment control-signal decoder
c0 c1 c2 c3 c4 c5 c6
A B C D
c1
c5
c2
c4
c6
c0
c3
The problem
  Input is a 4-bit BCD digit (A, B, C, D)
  Need signals to drive a display (7 outputs C0 – C6)

## Slide 17: Formalize the problem
A B C D C0 C1 C2 C3 C4 C5 C6
0 0 0 0 1 1 1 1 1 1 0
0 0 0 1 0 1 1 0 0 0 0
0 0 1 0 1 1 0 1 1 0 1
0 0 1 1 1 1 1 1 0 0 1
0 1 0 0 0 1 1 0 0 1 1
0 1 0 1 1 0 1 1 0 1 1
0 1 1 0 1 0 1 1 1 1 1
0 1 1 1 1 1 1 0 0 0 0
1 0 0 0 1 1 1 1 1 1 1
1 0 0 1 1 1 1 0 0 1 1
1 0 1 – – – – – – – –
1 1 – – – – – – – – –
Truth table
  Many don’t cares
Choose implementation target
  If ROM, we are done
  Don't cares imply PAL/PLA may be good choice
Implement design
  Minimize the logic
  Map into PAL/PLA

## Slide 18: Sum-of-products implementation
C0 = A + B D + C + B' D'
C1 = C' D' + C D + B'
C2 = B + C' + D
C3 = B' D' + C D' + B C' D + B' C
C4 = B' D' + C D'
C5 = A + C' D' + B D' + B C'
C6 = A + C D' + B C' + B' C
1 0 X 1
0 1 X 1 1 1 X X
1 1 X X
D
A
B
C
1 1 X 1
1 0 X 1 1 1 X X
1 0 X X
D
A
B
C
0 1 X 1
0 1 X 1 1 0 X X
1 1 X X
D
A
B
C
1 1 X 1
1 1 X 1 1 1 X X
0 1 X X
D
A
B
C
1 0 X 1
0 1 X 0 1 0 X X
1 1 X X
D
A
B
C
1 0 X 1
0 0 X 0 0 0 X X
1 1 X X
D
A
B
C
1 1 X 1
0 1 X 1 0 0 X X
0 1 X X
D
A
B
C
15 unique product terms if we minimize individually

## Slide 19: Better SOP implementation
C0 = BC'D + CD + B'D' + BCD' + A C1 = B'D + C'D' + CD + B'D' C2 = B'D + BC'D + C'D' + CD + BCD' C3 = BC'D + B'D + B'D' + BCD' C4 = B'D' + BCD' C5 = BC'D + C'D' + A + BCD' C6 = B'C + BC' + BCD' + A
C0 = A + BD + C + B'D'
C1 = C'D' + CD + B'
C2 = B + C' + D
C3 = B'D' + CD' + BC'D + B'C
C4 = B'D' + CD'
C5 = A + C'D' + BD' + BC'
C6 = A + CD' + BC' + B'C
C2
1 1 X 1
1 1 X 1 1 1 X X
0 1 X X
D
A
B
C
1 1 X 1
1 1 X 1 1 1 X X
0 1 X X
D
A
B
C
C2
Can do better than 15 product terms
  Share terms among outputs  only 9 unique product terms
    Each term not necessarily minimized

## Slide 20: PLA implementation
BC'
B'C
B'D
BC'D
C'D'
CD
B'D'
A
BCD'
A B C D
C0 C1 C2 C3 C4 C5 C6 C7
C0 = BC'D + CD + B'D' + BCD' + A C1 = B'D + C'D' + CD + B'D' C2 = B'D + BC'D + C'D' + CD + BCD' C3 = BC'D + B'D + B'D' + BCD' C4 = B'D' + BCD' C5 = BC'D + C'D' + A + BCD' C6 = B'C + BC' + BCD' + A

## Slide 21: Example: Logical function unit
C0 C1 C2 Function Comments 0 0 0 1 always 1 0 0 1 A + B logical OR 0 1 0 (A • B)' logical NAND 0 1 1 A xor B logical xor 1 0 0 A xnor B logical xnor 1 0 1 A • B logical AND 1 1 0 (A + B)' logical NOR 1 1 1 0 always 0
3 control inputs: C0, C1, C2 2 data inputs: A, B 1 output: F
Multipurpose functional block
  3 control inputs (C) specify function
  2 data inputs (operands) A and B
  1 output (same bit-width as input operands)

## Slide 22: Formalize the problem and solve
Implementation choice: multiplexer with discrete gates
C0 C1 C2 A B F
0 0 0 0 0 1
0 0 0 0 1 1
0 0 0 1 0 1
0 0 0 1 1 1
0 0 1 0 0 0
0 0 1 0 1 1
0 0 1 1 0 1
0 0 1 1 1 1
0 1 0 0 0 1
0 1 0 0 1 1
0 1 0 1 0 1
0 1 0 1 1 0
0 1 1 0 0 0
0 1 1 0 1 1
0 1 1 1 0 1
0 1 1 1 1 0
1 0 0 0 0 1
1 0 0 0 1 0
1 0 0 1 0 0
1 0 0 1 1 1
1 0 1 0 0 0
1 0 1 0 1 0
1 0 1 1 0 0
1 0 1 1 1 1
1 1 0 0 0 1
1 1 0 0 1 0
1 1 0 1 0 0
1 1 0 1 1 0
1 1 1 0 0 0
1 1 1 0 1 0
1 1 1 1 0 0
1 1 1 1 1 0
1 0
A B
A B
A B
C2
C0
C1
0 1 2 3 4 5 6 7
S2
8:1 MUX
S1
S0
F

## Slide 23: Pal Feature: Tri-stated outputs
Enable
(Active Low)

## Slide 24: Pal Feature: Individually Tri-stated outputs
Enable
(Active Low)

## Slide 25: Pal Feature: Feedback terms

## Slide 26: Pal Feature: Registered outputs

## Slide 27: Pal Feature: Registers with bypass multiplexers

## Slide 28: PALC22V10