## Slide 1: Overview
Last lecture
  deMorgan’s theorem
  NAND and NOR
  Canonical forms
    Sum-of-products (minterms)
    Product-of-sums (maxterms)
Today’s lecture
  Logic simplification
    Boolean cubes
    Karnaugh maps
Notes: Class rule: Interrupt when you don’t understand why we are doing something

## Slide 2: Goal: Simplify two-level combinational logic
Algebraic simplification
  not an algorithmic/systematic procedure
  how do you know when the minimum realization has been found?
Computer-aided design tools
  precise solutions require very long computation times (NP hard)
  heuristic methods employed – "educated guesses”
Hand methods are still relevant
  many real-world problems are solvable by hand

## Slide 3: Logic-function simplification
Key tool: The uniting theorem  A(B’+B) = A
The approach:
  Find subsets of the ON-set where some variables don’t change (the A’s above) and others do (the B’s above)
  Eliminate the changing variables (the B’s)
A B F
0 0 1
0 1 1
1 0 0
1 1 0
A has the same value in both on-set rows  keep A
B has a different value in the two rows  eliminate B
F = A'B'+A'B = A'(B+B') = A'
Notes: Goal: Simplification of two-level combinational logic
Algebraic simplification
  not an algorithmic/systematic procedure
  how do you know when the minimum realization has been found?
Computer-aided design tools
  precise solutions require very long computation times (NP hard)
  heuristic methods employed – "educated guesses"
Hand methods still relevant
  many real-world problems are solvable by hand

## Slide 4: Boolean cubes
Visualize when we can apply the uniting theorem
  n input variables = n-dimensional "cube"
1-cube
2-cube
3-cube
4-cube
X
X
Y
X
Y
Z
W
X
Y
Z
0
1
11
00
01
10
000
111
0000
1111
1000
0111
101
100
011
0100
0010
0011
1100
1011

## Slide 5: Mapping truth tables onto Boolean cubes
ON set = solid nodes
OFF set = empty nodes
A
B
00
01
F
11
10
Subcube (a line) comprises
two nodes
A varies within the subcube;
B does not
This subcube represents the literal B'
A B F
0 0 1
0 1 0
1 0 1
1 1 0

## Slide 6: Logic minimization using Boolean cubes
Uniting theorem = find reduced-dimensionality subcubes
Example: Binary full-adder carry-out logic
  On-set is covered by the OR of three 2-D subcubes
A B Cin Cout
0 0 0 0
0 0 1 0
0 1 0 0
0 1 1 1
1 0 0 0
1 0 1 1
1 1 0 1
1 1 1 1
111
A
B
Cin
000
101
(A'+A)BCin
AB(Cin'+Cin)
A(B+B')Cin
Cout = BCin+AB+ACin

## Slide 7: M-dimensional cubes in n-dimensional space
In a 3-cube (three variables):
  A 0-cube (a single node) yields a term in 3 literals
  A 1-cube (a line of two nodes) yields a term in 2 literals
  A 2-cube (a plane of four nodes) yields a term in 1 literal
  A 3-cube (a cube of eight nodes) yields a constant term "1"
F(A,B,C) = m(4,5,6,7)
On-set forms a square (a 2-D cube)
A is asserted (true) and unchanging
B and C vary
This subcube represents the literal A
A
B
C
000
111
101
100
011
010
110
Notes: an m-subcube within an n-cube (m < n) yields a term with n – m literals

## Slide 8: Karnaugh maps
Flat representation of Boolean cubes
  Easy to use for 2– 4 dimensions
  Hard for 4 – 6 dimensions
  Virtually impossible for 6+ dimensions
    Use CAD tools
Help visualize adjacencies
  On-set elements that have one variable changing are adjacent
    Unlike a truth-table
  Visual way to apply the uniting theorem
0 2
1 3
0
1
A
B
0
1
A B F
0 0 1
0 1 0
1 0 1
1 1 0
1
0
0
1
0
1
2
3

## Slide 9: K-map cell numbering
Gray–code: Only one bit changes between cells
  Example: 00  01  11  10
Layout for 2 – 4 dimension K-maps:
C
0 4 12 8
1 5 13 9
3 7 15 11
2 6 14 10
AB
CD
A
D
00
01
11
10
00
01
11
10
0 2 6 4
1 3 7 5
0
1
AB
A
00
01
11
10
C
B
B
C
0
1
A
B
0
1
0
1
3
2
A
B

## Slide 10: Adjacencies
Wrap–around at edges
  First column to last column
  Top row to bottom row
000
001
010
011
110
111
100
101
0
1
AB
A
00
01
11
10
C
B
C
A
B
C
000
111
101
100
001
011
010
0 2 6 4
1 3 7 5

## Slide 11: K-map minimization: 2 and 3 variables
F = B'
Cout = AB + BCin + ACin
F(A,B,C) = m(0,4,5,7)
= B'C'+AC
1 1
0 0
0
1
A
B
0
1
0 0 1 0
0 1 1 1
0
1
AB
A
00
01
11
10
Cin
B
1 0 0 1
0 0 1 1
0
1
AB
A
00
01
11
10
C
B
0 2 6 4
1 3 7 5
0 2 6 4
1 3 7 5
0
1
3
2

## Slide 12: K-map minimization (con’t)
F(A,B,C) = m(0,4,5,7)
= B'C'+AC
F'(A,B,C) = m(1,2,3,6)
= A’C + BC’
F(A,B,C) = ???
F'(A,B,C) = ???
1 0 1 1
0 0 1 1
0
1
AB
A
00
01
11
10
C
B
1 0 0 1
0 0 1 1
0
1
AB
A
00
01
11
10
C
B
0 2 6 4
1 3 7 5
0 2 6 4
1 3 7 5
Obtain the complement by covering 0s with subcubes

## Slide 13: K-map minimization: 4 variables
Minimize F(A,B,C,D) = m(0,2,3,5,6,7,8,10,11,14,15)
  Find the least number of subcubes, each as large as possible, that cover the ON-set
A
C
D
0000
1111
1000
0111
B
1 0 0 1
0 1 0 0
1 1 1 1
1 1 1 1
AB
CD
A
B
D
00
01
11
10
00
01
11
10
C
0 4 12 8
1 5 13 9
3 7 15 11
2 6 14 10

## Slide 14: Karnaugh map: 4-variable example (con’t)
Minimize F(A,B,C,D) = m(0,2,3,5,6,7,8,10,11,14,15)
Answer: F = C+A'BD+B'D'
A
C
D
0000
1111
1000
0111
B
1 0 0 1
0 1 0 0
1 1 1 1
1 1 1 1
AB
CD
A
B
D
00
01
11
10
00
01
11
10
C

## Slide 15: K-map class examples
AB
CD
00
01
11
10
00
01
11
10
F(A,B,C,D) = m(0,3,7,8,11,15)
F(A,B,C,D) = ???
F’(A,B,C,D) = ???
F(A,B,C) = m(0,3,6,7)
F(A,B,C) = ???
F'(A,B,C) = ???
0
1
AB
00
01
11
10
C

## Slide 16: Quiz results

## Slide 17
1. (10 pts) Express –3610 as an 8-bit twos-complement binary number.
36 = 0010 0100
invert 1101 1011
add 1 1
result 1101 1100
Answer: _1_ _1_ _0_ _1_ _1_ _1_ _0_ _0_
msb lsb

## Slide 18
2. Find the complement of F. Do not simplify the expression.
F=(A+B')(A'D' + E)+(AC' + BD)
Using the set of rules for complement (deMorgan’s), this turns out to be a one-step process. We get
F' =A'B+(A+D)E'(A' + C)(B' + D')

## Slide 19
3. Find the dual of F. Do not simplify the expression.
F=AB+(A' + C)(B+E')
Using the set of rules for duals (Duality), this turns out to be a one-step process. We get
FD =(A+B)(A'C+BE')