## Slide 1: Overview
Last lecture
  Introduction to finite-state machines
    Example: A sequence detector FSM
    Example: A vending machine FSM
Today
  A bigger example
    Ant-brain FSM

## Slide 2: Ant in a maze
Electronic ant, electronic maze
  Design the ant
exit
0,0
0,127
127,127
127,0
start

## Slide 3: Example: ant brain (Ward, MIT)
Sensors: L and R antennae, 1 if in touching wall
Actuators: F - forward step, TL/TR - turn left/right slightly
Goal: find way out of maze
Strategy: keep the wall on the right

## Slide 4: Example: ant brain (special case 1)
Left (L) Antenna touching the wall

## Slide 5: Example: ant brain (special case 2)
Ant Lost

## Slide 6: Example: ant brain (special case 2)
Ant Lost (another example

## Slide 7: Ant behavior
A: Following wall, touching Go forward, turning left slightly
B: Following wall, not touching Go forward, turning right slightly
C: Break in wall Go forward, turning right slightly
D: Hit wall again Back to state A
E: Wall in front Turn left until...
F: ...we are here, same as state B
G: Turn left until...
LOST: Forward until we touch something

## Slide 8: Goal: Find a way out of maze
Sensors on L and R antennae
  Sensor = “1” if touching wall; “0” if not touching wall
    L'R'  no wall
    L'R  wall on right
    LR'  wall on left
    LR  wall in front
    ***  exit
Movement:
  F  forward one step
  TL  turn left 90 degrees
  TR  turn right 90 degrees

## Slide 9: Notes & strategy
Notes
  Maze has no islands
  Corridors are wider than ant
  Don’t worry about startup
  Assume a Moore machine
  Assume D flip-flops
Strategy
  Partition your design into datapath and control
  Keep the wall on the right

## Slide 10: The ant’s behavior
S1: Right antenna touching Go forward
S2: Break in wall Turn right
S3: Left antenna touching Turn left
Reset
Done Flag
S0: Lost
Go forward
exit
exit

## Slide 11: The maze
Can have multiple walls
Example: 00001100
 Walls on South and East
Virtual maze
  128 × 128 grid
    Stored in memory
    16384 8-bit words
  YX is maze addresses
    X is the ant’s horizontal position (7 bits)
    Y is the ant’s vertical position (7 bits)
  Each memory location says
    00000001  No wall
    00000010  North wall
    00000100  West wall
    00001000  South wall
    00010000  East wall
    00100000  Exit

## Slide 12: Where do you start???
Don’t look ahead

## Slide 13: What you need
An FSM for the ant
  3 outputs
    Go forward
    Turn left
    Turn right
Two 7-bit registers for X and Y
  With preload, increment, decrement
A register to hold the ant’s heading
Logic to convert memory data to antennae info

## Slide 14: Recommendations
7-bit counters for X, Y
  Move horizontally: Increment or decrement X
  Move vertically: Increment or decrement Y
Shift register for heading
  N: 0001
  W: 0010
  S: 0100
  E: 1000
  Rotate right when ant turns right
  Rotate left when ant turns left
Combinational logic for antennae decoder

## Slide 15: Partition the design
Ant-Brain
FSM
Forward
Turn right
Turn left
Heading
(shift register)
North
South
East
West
X counter
Increment
Decrement
Preload
Y counter
Increment
Decrement
Preload
SRAM Address
Antennae
logic
SRAM
L
R
Maze
Data

## Slide 16: Design the ant-brain FSM
  1. State diagram and state-transition table
  2. State minimization
  3. State assignment (or state encoding)
  4. Minimize next-state logic
  5. Implement the design

## Slide 17: Step 1a: State diagram
S1: Right antenna touching Go forward
S2: Break in wall Turn right
S3: Left antenna touching Turn left
Reset
Done Flag
S0: Lost
Go forward
L’ R’
L
exit
exit
L’ R
L’ R
R
L
L’ R’
L

## Slide 18: Step 1b: State-transition table
Exit State L R Next State Output
1 Reset
0 S0 0 0 S0 F
0 1 S1 F
1 0 S3 F
1 1 S3 F
0 S1 0 0 S2 F
0 1 S1 F
1 0 S3 F
1 1 S3 F
0 S2 0 0 S0 TR
0 1 S0 TR
1 0 S0 TR
1 1 S0 TR
0 S3 0 0 S1 TL
0 1 S1 TL
1 0 S3 TL
1 1 S3 TL

## Slide 19: Step 2: State minimization
Two states are equivalent if they cannot be distinguished at the outputs of the FSM
  The outputs are the same for any input sequence
Two conditions for two states to be equivalent
  1) Outputs must be the same in both states
  2) Machine must transition to equivalent states for all inputs
Any equivalent states in our state diagram?

## Slide 20: Step 3: State encoding
Exit X Y L R X+ Y+ F TL TR
1 Reset
0 0 0 0 0 0 0 1 0 0
0 0 0 1 0 1 1 0 0
0 0 1 0 1 1 1 0 0
0 0 1 1 1 1 1 0 0
0 0 1 0 0 1 0 1 0 0
0 1 0 1 0 1 1 0 0
0 1 1 0 1 1 1 0 0
0 1 1 1 1 1 1 0 0
0 1 0 0 0 0 0 0 0 1
1 0 0 1 0 0 0 0 1
1 0 1 0 0 0 0 0 1
1 0 1 1 0 0 0 0 1
0 1 1 0 0 0 1 0 1 0
1 1 0 1 0 1 0 1 0
1 1 1 0 1 1 0 1 0
1 1 1 1 1 1 0 1 0
S0  00
S1  01
S2  10
S3  11

## Slide 21: Step 4: Minimize the logic
0 1 0 0
0 0 0 0
1 1 1 0
1 1 1 0
X
X+
Y
R
L
0 0 1 0
1 1 1 0
1 1 1 0
1 1 1 0
X
Y+
Y
R
L
1 1 0 0
1 1 0 0
1 1 0 0
1 1 0 0
X
F
Y
R
L
0 0 1 0
0 0 1 0
0 0 1 0
0 0 1 0
X
TL
Y
L
0 0 0 1
0 0 0 1
0 0 0 1
0 0 0 1
X
TR
Y
R
L

## Slide 22: Step 5: Implement the design
Ant-Brain FSM
X+ = LY+LX’+X’YR’
Y+ = XY+X’R+X’L
F = X’
TL = XY
TR = XY’
Forward
Turn
right
Turn
left
Heading
(shift register)
North
South
East
West
X counter
Forward
East
West
Y counter
SRAM Address
Turn
right
Turn
left
Preload
Forward
North
South
Preload
Antennae
logic
SRAM
L
R
Maze
Data
SRAM
Address
N S E W
L
R

## Slide 23: Antennae logic
  Each memory location says
    00000001  No wall
    00000010  North wall (NW)
    00000100  West wall (WW)
    00001000  South wall (SW)
    00010000  East wall (EW)
    00100000  Exit
  The ant can be heading
    N: 0001
    W: 0010
    S: 0100
    E: 1000
Logic for right antennae
R = NW(N + W) +
WW(W + S) +
SW(S + E) + EW(E + N)
Logic for left antennae
L = NW(N + E) +
WW(W + N) +
SW(S + W) + EW(E + S)
Gate count:
4 2-input ORs
8 2-input ANDs
2 4-input ORs

## Slide 24: What we left out...
Crumbs in cell
  Ant eats crumbs in every cell it visits
  Writes crumb file back to SRAM
  Read crumb file, for future display on monitor
Need a memory controller
  A state machine to talk to the SRAM
Need to deal with startup, exit states!

## Slide 25: Extra Credit:
Design the memory controller:
Due last day in class, Friday, June 1; printouts only
Value: up to 1 quiz
Graded on clarity and completeness of explanation
No questions will be answered
X counter
Forward
East
West
Y counter
SRAM Address
Preload
Forward
North
South
Preload