## Slide 1: Canonical forms
Last lecture
  Logic gates and truth tables
  Implementing logic functions
  CMOS switches
Today’s lecture
  deMorgan’s theorem
  NAND and NOR
  Canonical forms
    Sum-of-products (minterms)
    Product-of-sums (maxterms)
Notes: Class rule: Interrupt when you don’t understand why we are doing something

## Slide 2: de Morgan’s theorem
Replace
  • with +, + with •, 0 with 1, and 1 with 0
  All variables with their complements
Example 1: Z = A'B' + A'C'
  Z' = (A'B' + A'C')'
  = (A'B')' • (A'C')'
  = (A+B) • (A+C)
Example 2: Z = A'B'C + A'BC + AB'C + ABC'
  Z' = (A'B'C + A'BC + AB'C + ABC')'
  = (A'B'C)' • (A'BC)' • (AB'C)' • (ABC')'
  = (A+B+C') • (A+B'+C') • (A'+B+C') • (A'+B'+C)

## Slide 3: NAND and NOR
(X + Y)' = X' • Y' NOR is equivalent to AND with inputs complemented
(X • Y)' = X' + Y' NAND is equivalent to OR with inputs complemented
X Y X' Y' (X + Y)' X' • Y' 0 0 1 1 1 1 0 1 1 0 0 0 1 0 0 1 0 0
1 1 0 0 0 0
X Y X' Y' (X • Y)' X' + Y' 0 0 1 1 1 1 0 1 1 0 1 1 1 0 0 1 1 1
1 1 0 0 0 0

## Slide 4: NAND, NOR, and de Morgan’s theorum
de Morgan's
  Standard form: A'B' = (A + B)' A' + B' = (AB)'
  Inverted: A + B = (A'B')' (AB) = (A' + B')'
  AND with complemented inputs  NOR
  OR with complemented inputs  NAND
  OR  NAND with complemented inputs
  AND  NOR with complemented inputs
NAND
OR
AND
NOR
pushing
the bubble
NAND
OR
AND
NOR

## Slide 5: Converting between forms
Introduce inversions ("bubbles")
  Introduce bubbles in pairs
    Conserve inversions
    Do not alter logic function
Example
  AND/OR to NAND/NAND
A
B
C
D
Z
A
B
C
D
Z
NAND
NAND
NAND
Z = AB + CD
= (A'+B')'+(C'+D')'
= [(A'+B')(C'+D')]'
= [(AB)'(CD)']'

## Slide 6: Converting between forms (con’t)
Example: AND/OR network to NOR/NOR
conserve
"bubbles"
Z = AB+CD
= (A'+B')'+(C'+D')’
= [(A'+B')'+(C'+D')’]’’
= {[(A'+B')'+(C'+D')']'}'
A
B
C
D
Z
A’
B’
C’
D’
Z
NOR
NOR
NOR

## Slide 7: Converting between forms (con’t)
Example: OR/AND to NAND/NAND
A
B
C
D
Z
Z
A’
B’
C’
D’
NAND
NAND
NAND

## Slide 8: Converting between forms (con’t)
Example: OR/AND to NOR/NOR
A
B
C
D
Z
Z
A
B
C
D
NOR
NOR
NOR

## Slide 9: Why convert between forms?
CMOS logic gates are inverting
  Get NAND, NOR, NOT
  Don’t get AND, OR, Buffer
X Y Z 0 0 1 0 1 1 1 0 1
1 1 0
Z
X
1.8V
0V
Y
1.8V
X
Y
X
Z
1.8V
0V
Y
1.8V
X
Y
X
Y
Z
X
Y
Z

## Slide 10: Canonical forms
Canonical forms
  Standard forms for Boolean expressions
  Unique algebraic signatures
  Generally not the simplest forms
    Can be minimized
  Derived from truth table
Two canonical forms
  Sum-of-products (minterms)
  Product-of-sum (maxterms)

## Slide 11: Sum-of-products canonical form (SOP)
Also called disjunctive normal form (DNF)
  Commonly called a minterm expansion
A B C F F' 0 0 0 0 1
0 0 1 1 0
0 1 0 0 1
0 1 1 1 0
1 0 0 0 1
1 0 1 1 0
1 1 0 1 0
1 1 1 1 0
001 011 101 110 111 F = A'B'C + A'BC + AB'C + ABC' + ABC
F' = A'B'C' + A'BC' + AB'C'
minterm

## Slide 12: Minterms
short-hand notation
A B C minterms 0 0 0 A'B'C' m0
0 0 1 A'B'C m1
0 1 0 A'BC' m2
0 1 1 A'BC m3
1 0 0 AB'C' m4
1 0 1 AB'C m5
1 1 0 ABC' m6
1 1 1 ABC m7
F in canonical form: F(A,B,C) = m(1,3,5,6,7) = m1 + m3 + m5 + m6 + m7
= A'B'C+A'BC+AB'C+ABC'+ABC
canonical form  minimal form F(A,B,C) = A'B'C+A'BC+AB'C+ABC+ABC'
= (A'B'+A'B+AB'+AB)C+ABC’
= ((A' + A)(B' + B))C + ABC' = ABC' + C
= AB + C
Variables appears exactly once in each minterm
  In true or inverted form (but not both)
SIGMA

## Slide 13: Product-of-sums canonical form (POS)
Also called conjunctive normal form (CNF)
  Commonly called a maxterm expansion
A B C F F' 0 0 0 0 1
0 0 1 1 0
0 1 0 0 1
0 1 1 1 0
1 0 0 0 1
1 0 1 1 0
1 1 0 1 0
1 1 1 1 0
000 010 100 F = (A + B + C) (A + B' + C) (A' + B + C)
F' = (A+B+C')(A+B'+C')(A'+B+C')(A'+B'+C)(A'+B'+C')
maxterm

## Slide 14: Maxterms
A B C maxterms 0 0 0 A+B+C M0
0 0 1 A+B+C' M1
0 1 0 A+B'+C M2
0 1 1 A+B'+C' M3
1 0 0 A'+B+C M4
1 0 1 A'+B+C' M5
1 1 0 A'+B'+C M6
1 1 1 A'+B'+C' M7
short-hand notation
F in canonical form: F(A,B,C) = M(0,2,4) = M0 • M2 • M4
= (A+B+C)(A+B'+C)(A'+B+C)
canonical form  minimal form F(A,B,C) = (A+B+C)(A+B'+C)(A'+B+C)
= (A+B+C)(A+B'+C)•
(A+B+C)(A'+B+C)
= (A + C)(B + C)
Variables appears exactly once in each maxterm
  In true or inverted form (but not both)
PI

## Slide 15: Canonical implementations of F = AB + C

## Slide 16: SOP, POS, and de Morgan's theorem
Sum-of-products
  F' = A'B'C' + A'BC' + AB'C'
Apply de Morgan's to get POS
  (F')' = (A'B'C' + A'BC' + AB'C')'
  F = (A+B+C)(A+B'+C)(A'+B+C)
Product-of-sums
  F' = (A+B+C')(A+B'+C')(A'+B+C')(A'+B'+C)(A'+B'+C')
Apply de Morgan's to get SOP
  (F')' = ((A+B+C')(A+B'+C')(A'+B+C')(A'+B'+C)(A'+B'+C'))'
  F = A'B'C + A'BC + AB'C + ABC' + ABC

## Slide 17: Conversion between canonical forms
Minterm to maxterm
  Use maxterms that aren’t in minterm expansion
  F(A,B,C) = m(1,3,5,6,7) = M(0,2,4)
Maxterm to minterm
  Use minterms that aren’t in maxterm expansion
  F(A,B,C) = M(0,2,4) = m(1,3,5,6,7)
Minterm of F to minterm of F'
  Use minterms that don’t appear
  F(A,B,C) = m(1,3,5,6,7) F'(A,B,C) = m(0,2,4)
Maxterm of F to maxterm of F'
  Use maxterms that don’t appear
  F(A,B,C) = M(0,2,4) F'(A,B,C) = M(1,3,5,6,7)