## Slide 1: Computer organization
Computer design – an application of digital logic design procedures
Computer = processing unit + memory system
Processing unit = control + datapath
Control = finite state machine
  inputs = machine instruction, datapath conditions
  outputs = register transfer control signals, ALU operation codes
  instruction interpretation = instruction fetch, decode, execute
Datapath = functional units + registers
  functional units = ALU, multipliers, dividers, etc.
  registers = program counter, shifters, storage registers

## Slide 2: Structure of a computer
central processing unit (CPU)
instruction unit – instruction fetch and interpretation FSM
execution unit – functional units
and registers
address
read/write
data
Processor
Memory
System
Block diagram view
control signals
data conditions
Data Path
Control

## Slide 3: Registers
LD asserted during a lo-to-hi clock transition loads new data into FFs
OE asserted causes FF state to be connected to output pins; otherwise they are left unconnected (high impedance)
OE
Q7
Q6
Q5
Q4
Q3
Q2
Q1
Q0
LD
D7
D6
D5
D4
D3
D2
D1
D0
CLK
Selectively loaded – EN or LD input
Output enable – OE input
Multiple registers – group 4 or 8 in parallel

## Slide 4: Register transfer
Point-to-point connection
  dedicated wires
  muxes on inputs of each register
Common input from multiplexer
  load enables for each register
  control signals for multiplexer
Common bus with output enables
  output enables and load enables for each register
rt
MUX
rs
MUX
rd
MUX
R4
MUX
rs
MUX
rt
rd
R4
BUS
rs
rt
rd
R4

## Slide 5: Register files
RE
RB
RA
WE
WB
WA
D3
D2
D1
D0
Q3
Q2
Q1
Q0
Collections of registers in one package
  two-dimensional array of FFs
  address used as index to a particular word
  can have separate read and write addresses so can do both at same time
4 by 4 register file
  16 D-FFs
  organized as four words of four bits each
  write-enable (load)
  read-enable (output enable)

## Slide 6: Memories
RD
WR
A9
A8
A7
A6
A5
A4
A3
A2
A2
A1
A0
IO3
IO2
IO1
IO0
Larger collections of storage elements
  implemented not as FFs but as much more efficient latches
  high-density memories use 1 to 5 switches (transitors) per memory bit
Static RAM – 1024 words each 4 bits wide
  once written, memory holds forever (not true for denser dynamic RAM)
  address lines to select word (10 lines for 1024 words)
  read enable
    same as output enable
    often called chip select
    permits connection of many chips into larger array
  write enable (same as load enable)
  bi-directional data lines
    output when reading, input when writing

## Slide 7: Instruction sequencing
Example – an instruction to add the contents of two registers (Rx and Ry) and place result in a third register (Rz)
Step 1: get the ADD instruction from memory into an instruction register
Step 2: decode instruction
  instruction in IR has the code of an ADD instruction
  register indices used to generate output enables for registers Rx and Ry
  register index used to generate load signal for register Rz
Step 3: execute instruction
  enable Rx and Ry output and direct to ALU
  setup ALU to perform ADD operation
  direct result to Rz so that it can be loaded into register

## Slide 8: Instruction types
Data manipulation
  add, subtract
  increment, decrement
  multiply
  shift, rotate
  immediate operands
Data staging
  load/store data to/from memory
  register-to-register move
Control
  conditional/unconditional branches in program flow
  subroutine call and return

## Slide 9: Elements of the control unit (aka instruction unit)
Standard FSM elements
  state register
  next-state logic
  output logic (datapath/control signalling)
  Moore or synchronous Mealy machine to avoid loops unbroken by FF
Plus additional "control" registers
  instruction register (IR)
  program counter (PC)
Inputs/outputs
  outputs control elements of data path
  inputs from data path used to alter flow of program (test if zero)

## Slide 10: Instruction execution
Reset
Initialize Machine
Register- to-Register
Branch Not Taken
Branch Taken
Control state diagram (for each diagram)
  reset
  fetch instruction
  decode
  execute
Instructions partitioned into three classes
  branch
  load/store
  register-to-register
Different sequence through diagram for each instruction type
Init
Fetch Instr.
XEQ Instr.
Load/ Store
Branch
Incr. PC

## Slide 11: Data path (heirarchy)
Cin
Ain
Bin
Sum
Cout
FA
HA
Ain
Bin
Sum
Cin
Cout
HA
Arithmetic circuits constructed in hierarchical and iterative fashion
  each bit in datapath is functionally identical
  4-bit, 8-bit, 16-bit, 32-bit datapaths

## Slide 12: Data path (ALU)
16
16
A
B
S
Z
N
Operation
16
ALU block diagram
  input: data and operation to perform
  output: result of operation and status information

## Slide 13: Data path (ALU + registers)
16
Z
N
OP
16
AC
REG
16
16
Accumulator
  special register
  one of the inputs to ALU
  output of ALU stored back in accumulator
One-address instructions
  operation and address of one operand
  other operand and destination is accumulator register
  AC <– AC op Mem[addr]
  "single address instructions” (AC implicit operand)
Multiple registers
  part of instruction used to choose register operands

## Slide 14: Data path (bit-slice)
2 bits wide
1 bit wide
Bit-slice concept – iterate to build n-bit wide datapaths
CO
CI
ALU
AC
R0
from memory
rs
rt
rd
CO
ALU
AC
R0
from memory
rs
rt
rd
CI
ALU
AC
R0
from memory
rs
rt
rd

## Slide 15: Instruction path
Program counter
  keeps track of program execution
  address of next instruction to read from memory
  may have auto-increment feature or use ALU
Instruction register
  current instruction
  includes ALU operation and address of operand
  also holds target of jump instruction
  immediate operands
Relationship to data path
  PC may be incremented through ALU
  contents of IR may also be required as input to ALU

## Slide 16: Data path (memory interface)
Memory
  separate data and instruction memory (Harvard architecture)
    two address busses, two data busses
  single combined memory (Princeton architecture)
    single address bus, single data bus
Separate memory
  ALU output goes to data memory input
  register input from data memory output
  data memory address from instruction register
  instruction register from instruction memory output
  instruction memory address from program counter
Single memory
  address from PC or IR
  memory output to instruction and data registers
  memory input from ALU output

## Slide 17: Block diagram of processor
16
Z
N
OP
8
AC
REG
16
16
load
path
store path
Data Memory
(16-bit words)
16
OP
16
PC
IR
16
16
data
addr
rd wr
MAR
Control FSM
Register transfer view of Princeton architecture
  which register outputs are connected to which register inputs
  arrows represent data-flow, other are control signals from control FSM
  MAR may be a simple multiplexer rather than separate register
  MBR is split in two (REG and IR)
  load control for each register

## Slide 18: Block diagram of processor
Control FSM
16
16
Z
N
OP
16
AC
REG
16
load
path
store path
Data Memory
(16-bit words)
16
16
OP
16
PC
IR
16
data
addr
rd wr
Inst Memory
(8-bit words)
data
addr
Register transfer view of Harvard architecture
  which register outputs are connected to which register inputs
  arrows represent data-flow, other are control signals from control FSM
  two MARs (PC and IR)
  two MBRs (REG and IR)
  load control for each register

## Slide 19: A simplified processor data-path and memory
Princeton architecture
Register file
Instruction register
PC incremented through ALU
Modeled after MIPS rt000 (used in 378 textbook by Patterson & Hennessy)
  really a 32 bit machine
  we’ll do a 16 bit version
memory has only 255 words with a display on the last one

## Slide 20: Processor control
Synchronous Mealy machine
Multiple cycles per instruction

## Slide 21: Processor instructions
Three principal types (16 bits in each instruction) type op rs rt rd funct R(egister) 3 3 3 3 4 I(mmediate) 3 3 3 7 J(ump) 3 13
Some of the instructions add 0 rs rt rd 0 rd = rs + rt sub 0 rs rt rd 1 rd = rs - rt and 0 rs rt rd 2 rd = rs & rt or 0 rs rt rd 3 rd = rs | rt slt 0 rs rt rd 4 rd = (rs < rt) lw 1 rs rt offset rt = mem[rs + offset] sw 2 rs rt offset mem[rs + offset] = rt beq 3 rs rt offset pc = pc + offset, if (rs == rt) addi 4 rs rt offset rt = rs + offset j 5 target address pc = target address halt 7 - stop execution until reset
R
I
J

## Slide 22: Tracing an instruction's execution
Instruction: r3 = r1 + r2 R 0 rs=r1 rt=r2 rd=r3 funct=0
1. instruction fetch
  move instruction address from PC to memory address bus
  assert memory read
  move data from memory data bus into IR
  configure ALU to add 1 to PC
  configure PC to store new value from ALUout
2. instruction decode
  op-code bits of IR are input to control FSM
  rest of IR bits encode the operand addresses (rs and rt)
    these go to register file

## Slide 23: Tracing an instruction's execution (cont’d)
Instruction: r3 = r1 + r2 R 0 rs=r1 rt=r2 rd=r3 funct=0
3. instruction execute
  set up ALU inputs
  configure ALU to perform ADD operation
  configure register file to store ALU result (rd)

## Slide 24: Tracing an instruction's execution (cont’d)
Step 1

## Slide 25: Tracing an instruction's execution (cont’d)
Step 2
to controller

## Slide 26: Tracing an instruction's execution (cont’d)
Step 3

## Slide 27: Register-transfer-level description
Control
  transfer data between registers by asserting appropriate control signals
Register transfer notation - work from register to register
  instruction fetch: mabus  PC; – move PC to memory address bus (PCmaEN, ALUmaEN) memory read; – assert memory read signal (mr, RegBmdEN) IR  memory; – load IR from memory data bus (IRld) op  add – send PC into A input, 1 into B input, add (srcA, srcB0, scrB1, op) PC  ALUout – load result of incrementing in ALU into PC (PCld, PCsel)
  instruction decode: IR to controller values of A and B read from register file (rs, rt)
  instruction execution: op  add – send regA into A input, regB into B input, add (srcA, srcB0, scrB1, op) rd  ALUout – store result of add into destination register (regWrite, wrDataSel, wrRegSel)

## Slide 28: Register-transfer-level description (cont’d)
How many states are needed to accomplish these transfers?
  data dependencies (where do values that are needed come from?)
  resource conflicts (ALU, busses, etc.)
In our case, it takes three cycles
  one for each step
  all operation within a cycle occur between rising edges of the clock
How do we set all of the control signals to be output by the state machine?
  depends on the type of machine (Mealy, Moore, synchronous Mealy)

## Slide 29: Review of FSM timing
step 1
step 2
step 3
fetch
decode
execute
IR  mem[PC];
PC  PC + 1;
rd  A + B
A  rs
B  rt
to configure the data-path to do this here,
when do we set the control signals?

## Slide 30: FSM controller for CPU (skeletal Moore FSM)
instruction execution
instruction decode
LW
SW
ADD
J
reset
First pass at deriving the state diagram (Moore machine)
  these will be further refined into sub-states
instruction fetch

## Slide 31: FSM controller for CPU (reset and inst. fetch)
Assume Moore machine
  outputs associated with states rather than arcs
Reset state and instruction fetch sequence
On reset (go to Fetch state)
  start fetching instructions
  PC will set itself to zero mabus  PC; memory read; IR  memory data bus; PC  PC + 1;
reset
instruction fetch
Fetch

## Slide 32: FSM controller for CPU (decode)
Operation decode state
  next state branch based on operation code in instruction
  read two operands out of register file
    what if the instruction doesn’t have two operands?
instruction decode
Decode
branch based on value of Inst[15:13] and Inst[3:0]
add

## Slide 33: FSM controller for CPU (instruction execution)
For add instruction
  configure ALU and store result in register rd  A + B
  other instructions may require multiple cycles
instruction execution
add

## Slide 34: FSM controller for CPU (add instruction)
Putting it all together and closing the loop
  the famous instruction fetch decode execute cycle
reset
instruction fetch
Fetch
instruction decode
Decode
add
instruction execution
add

## Slide 35: FSM controller for CPU
Now we need to repeat this for all the instructions of our processor
  fetch and decode states stay the same
  different execution states for each instruction
    some may require multiple states if available register transfer paths require sequencing of steps