## Slide 1: Combinational logic
Basic logic
  Boolean algebra, proofs by re-writing, proofs by perfect induction
  Logic functions, truth tables, and switches
  NOT, AND, OR, NAND, NOR, XOR, . . ., minimal set
Logic realization
  two-level logic and canonical forms, incompletely specified functions
  multi-level logic, converting between ANDs and ORs
Simplification
  uniting theorem
  transformations on networks of Boolean functions
Time behavior
Hardware description languages

## Slide 2: Possible logic functions of two variables
        X Y 16 possible functions (F0–F15) 0 0 0 0 0 0 0 0 0 0 1 1 1 1 1 1 1 1 0 1 0 0 0 0 1 1 1 1 0 0 0 0 1 1 1 1
        1 0 0 0 1 1 0 0 1 1 0 0 1 1 0 0 1 1
        1 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1
0
X and Y
X
Y
X or Y
not Y
not X
1
X
Y
F
X xor Y
X nor Y not (X or Y)
X = Y
X nand Y not (X and Y)
There are 16 possible functions of 2 input variables:
  in general, there are 2**(2**n) functions of n inputs

## Slide 3: Cost of different logic functions
Different functions are easier or harder to implement
  each has a cost associated with the number of switches needed
  0 (F0) and 1 (F15): require 0 switches, directly connect output to low/high
  X (F3) and Y (F5): require 0 switches, output is one of inputs
  X’ (F12) and Y’ (F10): require 2 switches for "inverter" or NOT-gate
  X nor Y (F4) and X nand Y (F14): require 4 switches
  X or Y (F7) and X and Y (F1): require 6 switches
  X = Y (F9) and X  Y (F6): require 16 switches
  thus, because NOT, NOR, and NAND are the cheapest they are the functions we implement the most in practice

## Slide 4: Minimal set of functions
X Y X nand Y 0 0 1 1 1 0
X Y X nor Y 0 0 1 1 1 0
X nand Y  not ( (not X) nor (not Y) ) X nor Y  not ( (not X) nand (not Y) )
Can we implement all logic functions from NOT, NOR, and NAND?
  For example, implementing X and Y is the same as implementing not (X nand Y)
In fact, we can do it with only NOR or only NAND
  NOT is just a NAND or a NOR with both inputs tied together
  and NAND and NOR are "duals", that is, its easy to implement one using the other
But lets not move too fast . . .
  lets look at the mathematical foundation of logic

## Slide 5: An algebraic structure
An algebraic structure consists of
  a set of elements B
  binary operations { + , • }
  and a unary operation { ’ }
  such that the following axioms hold:
1. the set B contains at least two elements: a, b 2. closure: a + b is in B a • b is in B 3. commutativity: a + b = b + a a • b = b • a 4. associativity: a + (b + c) = (a + b) + c a • (b • c) = (a • b) • c 5. identity: a + 0 = a a • 1 = a 6. distributivity: a + (b • c) = (a + b) • (a + c) a • (b + c) = (a • b) + (a • c) 7. complementarity: a + a’ = 1 a • a’ = 0

## Slide 6: Boolean algebra
Boolean algebra
  B = {0, 1}
  variables
  + is logical OR, • is logical AND
  ’ is logical NOT
All algebraic axioms hold

## Slide 7: Logic functions and Boolean algebra
X, Y are Boolean algebra variables
X Y X • Y 0 0 0 0 1 0 1 0 0
1 1 1
X Y X’ Y’ X • Y X’ • Y’ ( X • Y ) + ( X’ • Y’ ) 0 0 1 1 0 1 1 0 1 1 0 0 0 0 1 0 0 1 0 0 0
1 1 0 0 1 0 1
( X • Y ) + ( X’ • Y’ )  X = Y
X Y X’ X’ • Y 0 0 1 0 0 1 1 1 1 0 0 0
1 1 0 0
Boolean expression that is true when the variables X and Y have the same value
and false, otherwise
Any logic function that can be expressed as a truth table can be written as an expression in Boolean algebra using the operators: ’, +, and •

## Slide 8: Axioms and theorems of Boolean algebra
identity 1. X + 0 = X 1D. X • 1 = X
null 2. X + 1 = 1 2D. X • 0 = 0
idempotency: 3. X + X = X 3D. X • X = X
involution: 4. (X’)’ = X
complementarity: 5. X + X’ = 1 5D. X • X’ = 0
commutativity: 6. X + Y = Y + X 6D. X • Y = Y • X
associativity: 7. (X + Y) + Z = X + (Y + Z) 7D. (X • Y) • Z = X • (Y • Z)

## Slide 9: Axioms and theorems of Boolean algebra (cont’d)
distributivity: 8. X • (Y + Z) = (X • Y) + (X • Z) 8D. X + (Y • Z) = (X + Y) • (X + Z)
uniting: 9. X • Y + X • Y’ = X 9D. (X + Y) • (X + Y’) = X
absorption: 10. X + X • Y = X 10D. X • (X + Y) = X 11. (X + Y’) • Y = X • Y 11D. (X • Y’) + Y = X + Y
factoring: 12. (X + Y) • (X’ + Z) = 12D. X • Y + X’ • Z = X • Z + X’ • Y (X + Z) • (X’ + Y)
concensus: 13. (X • Y) + (Y • Z) + (X’ • Z) = 13D. (X + Y) • (Y + Z) • (X’ + Z) = X • Y + X’ • Z (X + Y) • (X’ + Z)

## Slide 10: Axioms and theorems of Boolean algebra (cont’)
de Morgan’s: 14. (X + Y + ...)’ = X’ • Y’ • ... 14D. (X • Y • ...)’ = X’ + Y’ + ...
generalized de Morgan’s: 15. f’(X1,X2,...,Xn,0,1,+,•) = f(X1’,X2’,...,Xn’,1,0,•,+)
establishes relationship between • and +

## Slide 11: Axioms and theorems of Boolean algebra (cont’)
Duality
  a dual of a Boolean expression is derived by replacing • by +, + by •, 0 by 1, and 1 by 0, and leaving variables unchanged
  any theorem that can be proven is thus also proven for its dual!
  a meta-theorem (a theorem about theorems)
duality: 16. X + Y + ...  X • Y • ...
generalized duality: 17. f (X1,X2,...,Xn,0,1,+,•)  f(X1,X2,...,Xn,1,0,•,+)
Different than deMorgan’s Law
  this is a statement about theorems
  this is not a way to manipulate (re-write) expressions

## Slide 12: Proving theorems (rewriting)
Using the axioms of Boolean algebra:
  e.g., prove the theorem: X • Y + X • Y’ = X
  e.g., prove the theorem: X + X • Y = X
distributivity (8) X • Y + X • Y’ = X • (Y + Y’)
complementarity (5) X • (Y + Y’) = X • (1)
identity (1D) X • (1) = X 
identity (1D) X + X • Y = X • 1 + X • Y
distributivity (8) X • 1 + X • Y = X • (1 + Y)
identity (2) X • (1 + Y) = X • (1)
identity (1D) X • (1) = X 

## Slide 13: Activity
Prove the following using the laws of Boolean algebra:
  (X • Y) + (Y • Z) + (X’ • Z) = X • Y + X’ • Z
(X • Y) + (Y • Z) + (X’ • Z)
identity (X • Y) + (1) • (Y • Z) + (X’ • Z)
complementarity (X • Y) + (X’ + X) • (Y • Z) + (X’ • Z)
distributivity (X • Y) + (X’ • Y • Z) + (X • Y • Z) + (X’ • Z)
associativity (X • Y) + (X • Y • Z) + (X’ • Y • Z) + (X’ • Z)
factoring (X • Y) • (1 + Z) + (X’ • Z) • (1 + Y)
null (X • Y) • (1) + (X’ • Z) • (1)
identity (X • Y) + (X’ • Z) 

## Slide 14: Proving theorems (perfect induction)
(X + Y)’ = X’ • Y’ NOR is equivalent to AND with inputs complemented
(X • Y)’ = X’ + Y’ NAND is equivalent to OR with inputs complemented
X Y X’ Y’ (X + Y)’ X’ • Y’ 0 0 1 1 0 1 1 0
1 0 0 1
1 1 0 0
X Y X’ Y’ (X • Y)’ X’ + Y’ 0 0 1 1
0 1 1 0 1 0 0 1
1 1 0 0
Using perfect induction (complete truth table):
  e.g., de Morgan’s:
1
0
0
0
1
1
1
0
1
0
0
0
1
1
1
0

## Slide 15: A simple example: 1-bit binary adder
Inputs: A, B, Carry-in
Outputs: Sum, Carry-out
A
B
Cin
Cout
S
A B Cin S Cout
0 0 0 0 0 1
0 1 0
0 1 1
1 0 0 1 0 1
1 1 0
1 1 1
0
1
1
0
1
0
0
1
0
0
0
1
0
1
1
1
Cout = A’ B Cin + A B’ Cin + A B Cin’ + A B Cin
S = A’ B’ Cin + A’ B Cin’ + A B’ Cin’ + A B Cin

## Slide 16: Apply the theorems to simplify expressions
The theorems of Boolean algebra can simplify Boolean expressions
  e.g., full adder’s carry-out function (same rules apply to any function)
Cout = A’ B Cin + A B’ Cin + A B Cin’ + A B Cin
= A’ B Cin + A B’ Cin + A B Cin’ + A B Cin + A B Cin
= A’ B Cin + A B Cin + A B’ Cin + A B Cin’ + A B Cin
= (A’ + A) B Cin + A B’ Cin + A B Cin’ + A B Cin
= (1) B Cin + A B’ Cin + A B Cin’ + A B Cin
= B Cin + A B’ Cin + A B Cin’ + A B Cin + A B Cin
= B Cin + A B’ Cin + A B Cin + A B Cin’ + A B Cin
= B Cin + A (B’ + B) Cin + A B Cin’ + A B Cin
= B Cin + A (1) Cin + A B Cin’ + A B Cin
= B Cin + A Cin + A B (Cin’ + Cin)
= B Cin + A Cin + A B (1)
= B Cin + A Cin + A B
adding extra terms creates new factoring opportunities

## Slide 17: Activity
Fill in the truth-table for a circuit that checks that a 4-bit number is divisible by 2, 3, or 5
Write down Boolean expressions for By2, By3, and By5
X8 X4 X2 X1 By2 By3 By5
0 0 0 0 1 1 1
0 0 0 1 0 0 0
0 0 1 0 1 0 0
0 0 1 1 0 1 0

## Slide 18: Activity
X8 X4 X2 X1 By2 By3 By5
0 0 0 0 1 1 1
0 0 0 1 0 0 0
0 0 1 0 1 0 0
0 0 1 1 0 1 0
0 1 0 0 1 0 0
0 1 0 1 0 0 1
0 1 1 0 1 1 0
0 1 1 1 0 0 0
1 0 0 0 1 0 0
1 0 0 1 0 1 0
1 0 1 0 1 0 1
1 0 1 1 0 0 0
1 1 0 0 1 1 0
1 1 0 1 0 0 0
1 1 1 0 1 0 0
1 1 1 1 0 1 1
By2 = X8’X4’X2’X1’ + X8’X4’X2X1’
+ X8’X4X2’X1’ + X8’X4X2X1’ + X8X4’X2’X1’ + X8X4’X2X1’ + X8X4X2’X1’ + X8X4X2X1’
= X1’
By3 = X8’X4’X2’X1’ + X8’X4’X2X1
+ X8’X4X2X1’ + X8X4’X2’X1 + X8X4X2’X1’ + X8X4X2X1
By5 = X8’X4’X2’X1’ + X8’X4X2’X1
+ X8X4’X2X1’ + X8X4X2X1

## Slide 19: From Boolean expressions to logic gates
X Y Z 0 0 0 0 1 0 1 0 0
1 1 1
X Y 0 1 1 0
X Y Z 0 0 0 0 1 1 1 0 1
1 1 1
X
Y
X
X
Y
Y
Z
Z
NOT X’ X ~X
AND X • Y XY X  Y
OR X + Y X  Y

## Slide 20: From Boolean expressions to logic gates (cont’d)
X
Y
Z
X Y Z 0 0 1 0 1 1 1 0 1
1 1 0
X Y Z 0 0 1 0 1 0 1 0 0
1 1 0
Z
X
Y
X
Y
Z
X Y Z 0 0 1 0 1 0 1 0 0
1 1 1
X Y Z 0 0 0 0 1 1 1 0 1
1 1 0
Z
X
Y
X xor Y = X Y’ + X’ Y X or Y but not both ("inequality", "difference")
X xnor Y = X Y + X’ Y’ X and Y are the same ("equality", "coincidence")
NAND
NOR
XOR X Y
XNOR X = Y

## Slide 21: From Boolean expressions to logic gates (cont’d)
T1
T2
use of 3-input gate
A
B
C
D
T2
T1
Z
A
B
C
D
Z
More than one way to map expressions to gates
  e.g., Z = A’ • B’ • (C + D) = (A’ • (B’ • (C + D)))

## Slide 22: Waveform view of logic functions
time
change in Y takes time to "propagate" through gates
Just a sideways truth table
  but note how edges don’t line up exactly
  it takes time for a gate to switch its output!

## Slide 23: Choosing different realizations of a function
A B C Z 0 0 0 0
0 0 1 1
0 1 0 0
0 1 1 1
1 0 0 0
1 0 1 1
1 1 0 1
1 1 1 0
two-level realization (we don’t count NOT gates)
XOR gate (easier to draw but costlier to build)
multi-level realization (gates with fewer inputs)

## Slide 24: Which realization is best?
Reduce number of inputs
  literal: input variable (complemented or not)
    can approximate cost of logic gate as 2 transitors per literal
    why not count inverters?
  fewer literals means less transistors
    smaller circuits
  fewer inputs implies faster gates
    gates are smaller and thus also faster
  fan-ins (# of gate inputs) are limited in some technologies
Reduce number of gates
  fewer gates (and the packages they come in) means smaller circuits
    directly influences manufacturing costs

## Slide 25: Which is the best realization? (cont’d)
Reduce number of levels of gates
  fewer level of gates implies reduced signal propagation delays
  minimum delay configuration typically requires more gates
    wider, less deep circuits
How do we explore tradeoffs between increased circuit delay and size?
  automated tools to generate different solutions
  logic minimization: reduce number of gates and complexity
  logic optimization: reduction while trading off against delay

## Slide 26: Are all realizations equivalent?
Under the same input stimuli, the three alternative implementations have almost the same waveform behavior
  delays are different
  glitches (hazards) may arise
  variations due to differences in number of gate levels and structure
The three implementations are functionally equivalent

## Slide 27: Implementing Boolean functions
Technology independent
  canonical forms
  two-level forms
  multi-level forms
Technology choices
  packages of a few gates
  regular logic
  two-level programmable logic
  multi-level programmable logic

## Slide 28: Canonical forms
Truth table is the unique signature of a Boolean function
Many alternative gate realizations may have the same truth table
Canonical forms
  standard forms for a Boolean expression
  provides a unique algebraic signature

## Slide 29: Sum-of-products canonical forms
A B C F F’ 0 0 0 0 1
0 0 1 1 0
0 1 0 0 1
0 1 1 1 0
1 0 0 0 1
1 0 1 1 0
1 1 0 1 0
1 1 1 1 0
F =
F’ = A’B’C’ + A’BC’ + AB’C’
Also known as disjunctive normal form
Also known as minterm expansion
F = 001 011 101 110 111
+ A’BC
+ AB’C
+ ABC’
+ ABC
A’B’C

## Slide 30: Sum-of-products canonical form (cont’d)
short-hand notation for minterms of 3 variables
A B C minterms 0 0 0 A’B’C’ m0
0 0 1 A’B’C m1
0 1 0 A’BC’ m2
0 1 1 A’BC m3
1 0 0 AB’C’ m4
1 0 1 AB’C m5
1 1 0 ABC’ m6
1 1 1 ABC m7
F in canonical form: F(A, B, C) = m(1,3,5,6,7) = m1 + m3 + m5 + m6 + m7
= A’B’C + A’BC + AB’C + ABC’ + ABC
canonical form  minimal form F(A, B, C) = A’B’C + A’BC + AB’C + ABC + ABC’
      = (A’B’ + A’B + AB’ + AB)C + ABC’
      = ((A’ + A)(B’ + B))C + ABC’ = C + ABC’ = ABC’ + C
= AB + C
Product term (or minterm)
  ANDed product of literals – input combination for which output is true
  each variable appears exactly once, in true or inverted form (but not both)

## Slide 31: Product-of-sums canonical form
A B C F F’ 0 0 0 0 1
0 0 1 1 0
0 1 0 0 1
0 1 1 1 0
1 0 0 0 1
1 0 1 1 0
1 1 0 1 0
1 1 1 1 0
F = 000 010 100 F =
F’ = (A + B + C’) (A + B’ + C’) (A’ + B + C’) (A’ + B’ + C) (A’ + B’ + C’)
Also known as conjunctive normal form
Also known as maxterm expansion
(A + B + C)
(A + B’ + C)
(A’ + B + C)

## Slide 32: Product-of-sums canonical form (cont’d)
A B C maxterms 0 0 0 A+B+C M0
0 0 1 A+B+C’ M1
0 1 0 A+B’+C M2
0 1 1 A+B’+C’ M3
1 0 0 A’+B+C M4
1 0 1 A’+B+C’ M5
1 1 0 A’+B’+C M6
1 1 1 A’+B’+C’ M7
short-hand notation for maxterms of 3 variables
F in canonical form: F(A, B, C) = M(0,2,4) = M0 • M2 • M4
= (A + B + C) (A + B’ + C) (A’ + B + C)
canonical form  minimal form F(A, B, C) = (A + B + C) (A + B’ + C) (A’ + B + C)
      = (A + B + C) (A + B’ + C)
      (A + B + C) (A’ + B + C)
      = (A + C) (B + C)
Sum term (or maxterm)
  ORed sum of literals – input combination for which output is false
  each variable appears exactly once, in true or inverted form (but not both)

## Slide 33: S-o-P, P-o-S, and de Morgan’s theorem
Sum-of-products
  F’ = A’B’C’ + A’BC’ + AB’C’
Apply de Morgan’s
  (F’)’ = (A’B’C’ + A’BC’ + AB’C’)’
  F = (A + B + C) (A + B’ + C) (A’ + B + C)
Product-of-sums
  F’ = (A + B + C’) (A + B’ + C’) (A’ + B + C’) (A’ + B’ + C) (A’ + B’ + C’)
Apply de Morgan’s
  (F’)’ = ( (A + B + C’)(A + B’ + C’)(A’ + B + C’)(A’ + B’ + C)(A’ + B’ + C’) )’
  F = A’B’C + A’BC + AB’C + ABC’ + ABC

## Slide 34: Four alternative two-level implementations of F = AB + C
canonical sum-of-products minimized sum-of-products canonical product-of-sums minimized product-of-sums
F1
F2
F3
B
A
C
F4

## Slide 35: Waveforms for the four alternatives
Waveforms are essentially identical
  except for timing hazards (glitches)
  delays almost identical (modeled as a delay per level, not type of gate or number of inputs to gate)

## Slide 36: Mapping between canonical forms
Minterm to maxterm conversion
  use maxterms whose indices do not appear in minterm expansion
  e.g., F(A,B,C) = m(1,3,5,6,7) = M(0,2,4)
Maxterm to minterm conversion
  use minterms whose indices do not appear in maxterm expansion
  e.g., F(A,B,C) = M(0,2,4) = m(1,3,5,6,7)
Minterm expansion of F to minterm expansion of F’
  use minterms whose indices do not appear
  e.g., F(A,B,C) = m(1,3,5,6,7) F’(A,B,C) = m(0,2,4)
Maxterm expansion of F to maxterm expansion of F’
  use maxterms whose indices do not appear
  e.g., F(A,B,C) = M(0,2,4) F’(A,B,C) = M(1,3,5,6,7)

## Slide 37: Incompleteley specified functions
A B C D W X Y Z 0 0 0 0 0 0 0 1
0 0 0 1 0 0 1 0
0 0 1 0 0 0 1 1
0 0 1 1 0 1 0 0
0 1 0 0 0 1 0 1
0 1 0 1 0 1 1 0
0 1 1 0 0 1 1 1
0 1 1 1 1 0 0 0
1 0 0 0 1 0 0 1
1 0 0 1 0 0 0 0
1 0 1 0 X X X X
1 0 1 1 X X X X
1 1 0 0 X X X X
1 1 0 1 X X X X
1 1 1 0 X X X X
1 1 1 1 X X X X
off-set of W
these inputs patterns should never be encountered in practice – "don’t care" about associated output values, can be exploited in minimization
Example: binary coded decimal increment by 1
  BCD digits encode the decimal digits 0 – 9 in the bit patterns 0000 – 1001
don’t care (DC) set of W
on-set of W

## Slide 38: Notation for incompletely specified functions
Don’t cares and canonical forms
  so far, only represented on-set
  also represent don’t-care-set
  need two of the three sets (on-set, off-set, dc-set)
Canonical representations of the BCD increment by 1 function:
  Z = m0 + m2 + m4 + m6 + m8 + d10 + d11 + d12 + d13 + d14 + d15
  Z =  [ m(0,2,4,6,8) + d(10,11,12,13,14,15) ]
  Z = M1 • M3 • M5 • M7 • M9 • D10 • D11 • D12 • D13 • D14 • D15
  Z =  [ M(1,3,5,7,9) • D(10,11,12,13,14,15) ]

## Slide 39: Simplification of two-level combinational logic
Finding a minimal sum of products or product of sums realization
  exploit don’t care information in the process
Algebraic simplification
  not an algorithmic/systematic procedure
  how do you know when the minimum realization has been found?
Computer-aided design tools
  precise solutions require very long computation times, especially for functions with many inputs (> 10)
  heuristic methods employed – "educated guesses" to reduce amount of computation and yield good if not best solutions
Hand methods still relevant
  to understand automatic tools and their strengths and weaknesses
  ability to check results (on small examples)

## Slide 40: The uniting theorem
A B F
0 0 1
0 1 0
1 0 1
1 1 0
B has the same value in both on-set rows – B remains
A has a different value in the two rows – A is eliminated
F = A’B’+AB’ = (A’+A)B’ = B’
Key tool to simplification: A (B’ + B) = A
Essence of simplification of two-level logic
  find two element subsets of the ON-set where only one variable changes its value – this single varying variable can be eliminated and a single product term used to represent both elements

## Slide 41: Implementations of two-level logic
Sum-of-products
  AND gates to form product terms (minterms)
  OR gate to form sum
Product-of-sums
  OR gates to form sum terms (maxterms)
  AND gates to form product

## Slide 42: Two-level logic using NAND gates
Replace minterm AND gates with NAND gates
Place compensating inversion at inputs of OR gate

## Slide 43: Two-level logic using NAND gates (cont’d)
OR gate with inverted inputs is a NAND gate
  de Morgan’s: A’ + B’ = (A • B)’
Two-level NAND-NAND network
  inverted inputs are not counted
  in a typical circuit, inversion is done once and signal distributed

## Slide 44: Two-level logic using NOR gates
Replace maxterm OR gates with NOR gates
Place compensating inversion at inputs of AND gate

## Slide 45: Two-level logic using NOR gates (cont’d)
AND gate with inverted inputs is a NOR gate
  de Morgan’s: A’ • B’ = (A + B)’
Two-level NOR-NOR network
  inverted inputs are not counted
  in a typical circuit, inversion is done once and signal distributed

## Slide 46: Two-level logic using NAND and NOR gates
OR
NAND
NAND
OR
AND
NOR
NOR
AND
NAND-NAND and NOR-NOR networks
  de Morgan’s law: (A + B)’ = A’ • B’ (A • B)’ = A’ + B’
  written differently: A + B = (A’ • B’)’ (A • B) = (A’ + B’)’
In other words ––
  OR is the same as NAND with complemented inputs
  AND is the same as NOR with complemented inputs
  NAND is the same as OR with complemented inputs
  NOR is the same as AND with complemented inputs

## Slide 47: Conversion between forms
A
B
C
D
Z
A
B
C
D
Z
NAND
NAND
NAND
Convert from networks of ANDs and ORs to networks of NANDs and NORs
  introduce appropriate inversions ("bubbles")
Each introduced "bubble" must be matched by a corresponding "bubble"
  conservation of inversions
  do not alter logic function
Example: AND/OR to NAND/NAND

## Slide 48: Conversion between forms (cont’d)
Z = [ (A • B)’ • (C • D)’ ]’
= [ (A’ + B’) • (C’ + D’) ]’
= [ (A’ + B’)’ + (C’ + D’)’ ]
= (A • B) + (C • D) 
Example: verify equivalence of two forms
A
B
C
D
Z
A
B
C
D
Z
NAND
NAND
NAND

## Slide 49: Conversion between forms (cont’d)
Step 2
conserve
"bubbles"
Step 1
conserve
"bubbles"
NOR
NOR
NOR
\A
\B
\C
\D
Z
NOR
NOR
A
B
C
D
Z
Example: map AND/OR network to NOR/NOR network
A
B
C
D
Z

## Slide 50: Conversion between forms (cont’d)
Z = { [ (A’ + B’)’ + (C’ + D’)’ ]’ }’
= { (A’ + B’) • (C’ + D’) }’
= (A’ + B’)’ + (C’ + D’)’
= (A • B) + (C • D) 
Example: verify equivalence of two forms
A
B
C
D
Z
NOR
NOR
NOR
\A
\B
\C
\D
Z

## Slide 51: Multi-level logic
A
B C
D E F G
X
x = A D F + A E F + B D F + B E F + C D F + C E F + G
  reduced sum-of-products form – already simplified
  6 x 3-input AND gates + 1 x 7-input OR gate (that may not even exist!)
  25 wires (19 literals plus 6 internal wires)
x = (A + B + C) (D + E) F + G
  factored form – not written as two-level S-o-P
  1 x 3-input OR gate, 2 x 2-input OR gates, 1 x 3-input AND gate
  10 wires (7 literals plus 3 internal wires)

## Slide 52: Conversion of multi-level logic to NAND gates
Level 1 Level 2 Level 3 Level 4
original
AND-OR network
A
C
D
B
B
\C
F
introduction and
conservation of bubbles
A
C
D
B
B
\C
F
redrawn in terms
of conventional
NAND gates
A
C
D
\B
B
\C
F
F = A (B + C D) + B C’

## Slide 53: Conversion of multi-level logic to NORs
Level 1 Level 2 Level 3 Level 4
A
C
D
B
B
\C
F
original
AND-OR network
introduction and
conservation of bubbles
A
C
D
B
B
\C
F
redrawn in terms
of conventional
NOR gates
\A
\C
\D
B
\B
C
F
F = A (B + C D) + B C’

## Slide 54: Conversion between forms
A
X
B
C
D
F
(a)
original circuit
A
X
B
C
D
F
(b)
add double bubbles at inputs
\D
A
\X
B
C
F
(c)
distribute bubbles
some mismatches
\D
A
X
B
C
F
\X
(d)
insert inverters to fix mismatches
Example

## Slide 55: AND-OR-invert gates
&
&
+
2x2 AOI gate
symbol
&
&
+
3x2 AOI gate
symbol
NAND NAND
Invert
possible implementation
A
B
C
D
Z
AND
OR Invert
logical concept
A
B
C
D
Z
AOI function: three stages of logic — AND, OR, Invert
  multiple gates "packaged" as a single circuit block

## Slide 56: Conversion to AOI forms
&
&
+
A’
B’
A
B
F
General procedure to place in AOI form
  compute the complement of the function in sum-of-products form
  by grouping the 0s in the Karnaugh map
Example: XOR implementation –– A xor B = A’ B + A B’
  AOI form: F = (A’ B’ + A B)’

## Slide 57: Examples of using AOI gates
each implemented in a single 2x2 AOI gate
Example:
  F = B C’ + A C’ + A B
  F’ = A’ B’ + A’ C + B’ C
  Implemented by 2-input 3-stack AOI gate
  F = (A + B) (A + C’) (B + C’)
  F’ = (B’ + C) (A’ + C) (A’ + B’)
  Implemented by 2-input 3-stack OAI gate
Example: 4-bit equality function
  Z = (A0 B0 + A0’ B0’)(A1 B1 + A1’ B1’)(A2 B2 + A2’ B2’)(A3 B3 + A3’ B3’)

## Slide 58: Examples of using AOI gates (cont’d)
high if A0  B0 low if A0 = B0
if all inputs are low
then Ai = Bi, i=0,...,3
output Z is high
conservation of bubbles
A0
B0
A1
B1
A2
B2
A3
B3
&
&
+
&
&
+
&
&
+
&
&
+
NOR
Z
Example: AOI implementation of 4-bit equality function

## Slide 59: Summary for multi-level logic
Advantages
  circuits may be smaller
  gates have smaller fan-in
  circuits may be faster
Disadvantages
  more difficult to design
  tools for optimization are not as good as for two-level
  analysis is more complex

## Slide 60: Time behavior of combinational networks
Waveforms
  visualization of values carried on signal wires over time
  useful in explaining sequences of events (changes in value)
Simulation tools are used to create these waveforms
  input to the simulator includes gates and their connections
  input stimulus, that is, input signal waveforms
Some terms
  gate delay — time for change at input to cause change at output
    min delay – typical/nominal delay – max delay
    careful designers design for the worst case
  rise time — time for output to transition from low to high voltage
  fall time — time for output to transition from high to low voltage
  pulse width — time that an output stays high or stays low between changes

## Slide 61: Momentary changes in outputs
F is not always 0
pulse 3 gate-delays wide
D remains high for
three gate delays after
A changes from low to high
F
A
B
C
D
Can be useful — pulse shaping circuits
Can be a problem — incorrect circuit operation (glitches/hazards)
Example: pulse shaping circuit
  A’ • A = 0
  delays matter in function

## Slide 62: Oscillatory behavior
initially undefined
close switch
open switch
+
open switch
resistor
A
B
C
D
Another pulse shaping circuit

## Slide 63: Hardware description languages
Describe hardware at varying levels of abstraction
Structural description
  textual replacement for schematic
  hierarchical composition of modules from primitives
Behavioral/functional description
  describe what module does, not how
  synthesis generates circuit for module
Simulation semantics

## Slide 64: HDLs
Abel (circa 1983) - developed by Data-I/O
  targeted to programmable logic devices
  not good for much more than state machines
ISP (circa 1977) - research project at CMU
  simulation, but no synthesis
Verilog (circa 1985) - developed by Gateway (absorbed by Cadence)
  similar to Pascal and C
  delays is only interaction with simulator
  fairly efficient and easy to write
  IEEE standard
VHDL (circa 1987) - DoD sponsored standard
  similar to Ada (emphasis on re-use and maintainability)
  simulation semantics visible
  very general but verbose
  IEEE standard

## Slide 65: Verilog
Supports structural and behavioral descriptions
Structural
  explicit structure of the circuit
  e.g., each logic gate instantiated and connected to others
Behavioral
  program describes input/output behavior of circuit
  many structural implementations could have same behavior
  e.g., different implementation of one Boolean function
We’ll only be using behavioral Verilog in DesignWorks
  rely on schematic when we want structural descriptions

## Slide 66: Structural model
module xor_gate (out, a, b); input a, b; output out; wire abar, bbar, t1, t2; inverter invA (abar, a); inverter invB (bbar, b); and_gate and1 (t1, a, bbar); and_gate and2 (t2, b, abar); or_gate or1 (out, t1, t2);
endmodule

## Slide 67: Simple behavioral model
module xor_gate (out, a, b); input a, b; output out;
reg out;
assign #6 out = a ^ b;
endmodule
Continuous assignment
delay from input change to output change
simulation register - keeps track of value of signal

## Slide 68: Simple behavioral model
module xor_gate (out, a, b); input a, b; output out; reg out; always @(a or b) begin
#6 out = a ^ b;
end
endmodule
always block
specifies when block is executed ie. triggered by which signals

## Slide 69: Driving a simulation
module stimulus (x, y); output x, y; reg [1:0] cnt; initial begin cnt = 0; repeat (4) begin #10 cnt = cnt + 1; $display ("@ time=%d, x=%b, y=%b, cnt=%b", $time, x, y, cnt); end #10 $finish; end assign x = cnt[1];
assign y = cnt[0]; endmodule
2-bit vector
initial block executed only once at start of simulation
directive to stop simulation
print to a console

## Slide 70: Complete Simulation
Instantiate stimulus component and device to test in a schematic
x
y
a
b
z

## Slide 71: Comparator Example
module Compare1 (A, B, Equal, Alarger, Blarger); input A, B; output Equal, Alarger, Blarger; assign #5 Equal = (A & B) | (~A & ~B); assign #3 Alarger = (A & ~B); assign #3 Blarger = (~A & B);
endmodule

## Slide 72: More Complex Behavioral Model
module life (n0, n1, n2, n3, n4, n5, n6, n7, self, out); input n0, n1, n2, n3, n4, n5, n6, n7, self; output out; reg out; reg [7:0] neighbors;
reg [3:0] count; reg [3:0] i; assign neighbors = {n7, n6, n5, n4, n3, n2, n1, n0};
always @(neighbors or self) begin count = 0; for (i = 0; i < 8; i = i+1) count = count + neighbors[i]; out = (count == 3); out = out | ((self == 1) & (count == 2)); end
endmodule

## Slide 73: Hardware Description Languages vs. Programming Languages
Program structure
  instantiation of multiple components of the same type
  specify interconnections between modules via schematic
  hierarchy of modules (only leaves can be HDL in DesignWorks)
Assignment
  continuous assignment (logic always computes)
  propagation delay (computation takes time)
  timing of signals is important (when does computation have its effect)
Data structures
  size explicitly spelled out - no dynamic structures
  no pointers
Parallelism
  hardware is naturally parallel (must support multiple threads)
  assignments can occur in parallel (not just sequentially)

## Slide 74: Hardware Description Languages and Combinational Logic
Modules - specification of inputs, outputs, bidirectional, and internal signals
Continuous assignment - a gate’s output is a function of its inputs at all times (doesn’t need to wait to be "called")
Propagation delay- concept of time and delay in input affecting gate output
Composition - connecting modules together with wires
Hierarchy - modules encapsulate functional blocks
Specification of don’t care conditions (accomplished by setting output to “x”)

## Slide 75: Combinational logic summary
Logic functions, truth tables, and switches
  NOT, AND, OR, NAND, NOR, XOR, . . ., minimal set
Axioms and theorems of Boolean algebra
  proofs by re-writing and perfect induction
Gate logic
  networks of Boolean functions and their time behavior
Canonical forms
  two-level and incompletely specified functions
Simplification
  two-level simplification
Later
  automation of simplification
  multi-level logic
  design case studies
  time behavior