## Slide 1: Sequential logic implementation
Finite-state machines
  Moore
  Mealy
  Synchronous Mealy
Implementation
  random logic gates and FFs
  programmable logic devices (PAL with FFs)
Design procedure
  state diagrams
  state transition table
  state assignment
  next state functions

## Slide 2: Implementation using PALs
D Q
Q
Programmable logic building block for sequential logic
  macro-cell: FF + logic
    D-FF
    two-level logic capability like PAL (e.g., 8 product terms)

## Slide 3: Comparison of Mealy and Moore machines
Mealy machines tend to have less states
  different outputs on arcs (n^2) rather than states (n)
Moore machines are safer to use
  outputs change at clock edge (always one cycle later)
  in Mealy machines, input change can cause output change as soon as logic is done – a big problem when two machines are interconnected – asynchronous feedback
Mealy machines react faster to inputs
  react in same cycle – don't need to wait for clock
  in Moore machines, more logic may be necessary to decode state into outputs – more gate delays after

## Slide 4: Comparison of Mealy and Moore machines (cont’d)
Moore
Mealy
Synchronous Mealy
state feedback
inputs
outputs
reg
combinational logic for next state
logic for outputs
inputs
outputs
state feedback
reg
combinational logic for next state
logic for outputs
inputs
outputs
state feedback
reg
combinational logic for next state
logic for outputs

## Slide 5: Example: vending machine
Vending Machine FSM
N
D
Reset
Clock
Open
Coin Sensor
Release Mechanism
Release item after 15 cents are deposited
Single coin slot for dimes, nickels
No change

## Slide 6: Example: vending machine (cont’d)
Suitable abstract representation
  tabulate typical input sequences:
    3 nickels
    nickel, dime
    dime, nickel
    two dimes
  draw state diagram:
    inputs: N, D, reset
    output: open chute
  assumptions:
    assume N and D asserted for one cycle
    each state has a self loop for N = D = 0 (no coin)
S0
Reset
S2
D
S6
[open]
D
S4
[open]
D
S1
N
S3
N
S5
[open]
N
S8
[open]
D
S7
[open]
N

## Slide 7: Example: vending machine (cont’d)
Minimize number of states - reuse states whenever possible
symbolic state table
present inputs next output state D N state open 0¢ 0 0 0¢ 0 0 1 5¢ 0 1 0 10¢ 0 1 1 – – 5¢ 0 0 5¢ 0 0 1 10¢ 0 1 0 15¢ 0 1 1 – – 10¢ 0 0 10¢ 0 0 1 15¢ 0 1 0 15¢ 0 1 1 – – 15¢ – – 15¢ 1
0¢
Reset
5¢
N
N
N + D
10¢
D
15¢
[open]
D

## Slide 8: Example: vending machine (cont’d)
present state inputs next state output Q1 Q0 D N D1 D0 open 0 0 0 0 0 0 0 0 1 0 1 0 1 0 1 0 0 1 1 – – – 0 1 0 0 0 1 0 0 1 1 0 0 1 0 1 1 0 1 1 – – – 1 0 0 0 1 0 0 0 1 1 1 0 1 0 1 1 0 1 1 – – – 1 1 – – 1 1 1
Uniquely encode states

## Slide 9: Example: Moore implementation
D1 = Q1 + D + Q0 N
D0 = Q0’ N + Q0 N’ + Q1 N + Q1 D
OPEN = Q1 Q0
Mapping to logic
0 0 1 1
0 1 1 1
X X X X
1 1 1 1
Q1
D1
Q0
N
D
0 1 1 0
1 0 1 1
X X X X
0 1 1 1
Q1
D0
Q0
N
D
0 0 1 0
0 0 1 0
X X 1 X
0 0 1 0
Q1
Open
Q0
N
D

## Slide 10: Example: vending machine (cont’d)
present state inputs next state output Q3 Q2 Q1 Q0 D N D3 D2 D1 D0 open 0 0 0 1 0 0 0 0 0 1 0 0 1 0 0 1 0 0 1 0 0 1 0 0 0 1 1 - - - - - 0 0 1 0 0 0 0 0 1 0 0 0 1 0 1 0 0 0 1 0 1 0 0 0 0 1 1 - - - - - 0 1 0 0 0 0 0 1 0 0 0 0 1 1 0 0 0 0 1 0 1 0 0 0 0 1 1 - - - - - 1 0 0 0 - - 1 0 0 0 1
D0 = Q0 D’ N’
D1 = Q0 N + Q1 D’ N’
D2 = Q0 D + Q1 N + Q2 D’ N’
D3 = Q1 D + Q2 D + Q2 N + Q3
OPEN = Q3
One-hot encoding

## Slide 11: Equivalent Mealy and Moore state diagrams
Moore machine
  outputs associated with state
0¢
[0]
10¢
[0]
5¢
[0]
15¢
[1]
N’ D’ + Reset
D
D
N
N+D
N
N’ D’
Reset’
N’ D’
N’ D’
Reset
0¢
10¢
5¢
15¢
(N’ D’ + Reset)/0
D/0
D/1
N/0
N+D/1
N/0
N’ D’/0
Reset’/1
N’ D’/0
N’ D’/0
Reset/0
Mealy machine
  outputs associated with transitions

## Slide 12: Vending machine example (Moore PLD mapping)
D0 = reset'(Q0'N + Q0N' + Q1N + Q1D)
D1 = reset'(Q1 + D + Q0N)
OPEN = Q1Q0
D
Q
D
Q
D
Q
Q0
Q1
Open
Com
Seq
Seq
CLK
N
D
Reset

## Slide 13: Example: Mealy implementation
0¢
10¢
5¢
15¢
(N’ D’ + Reset)/0
D/0
D/1
N/0
N+D/1
N/0
N’ D’/0
Reset’/1
N’ D’/0
N’ D’/0
Reset/0
present state inputs next state output Q1 Q0 D N D1 D0 open 0 0 0 0 0 0 0 0 1 0 1 0 1 0 1 0 0 1 1 – – – 0 1 0 0 0 1 0 0 1 1 0 0 1 0 1 1 1 1 1 – – – 1 0 0 0 1 0 0 0 1 1 1 1 1 0 1 1 1 1 1 – – – 1 1 – – 1 1 1
D0 = reset’(Q0’N + Q0N’ + Q1N + Q1D)
D1 = reset’(Q1 + D + Q0N)
OPEN = reset’(Q1Q0 + Q1N + Q1D + Q0D)
0 0 1 0
0 0 1 1
X X 1 X
0 1 1 1
Q1
Open
Q0
N
D

## Slide 14: Example: Mealy implementation
D0 = reset’(Q0’N + Q0N’ + Q1N + Q1D)
D1 = reset’(Q1 + D + Q0N)
OPEN = reset’(Q1Q0 + Q1N + Q1D + Q0D)

## Slide 15: Vending machine: Moore to synch. Mealy
OPEN = Q1Q0 creates a combinational delay after Q1 and Q0 change in Moore implementation
This can be corrected by retiming, i.e., move flip-flops and logic through each other to improve delay
OPEN = reset'(Q1 + D + Q0N)(Q0'N + Q0N' + Q1N + Q1D) = reset'(Q1Q0N' + Q1N + Q1D + Q0'ND + Q0N'D)
Implementation now looks like a synchronous Mealy machine
  it is common for programmable devices to have FF at end of logic

## Slide 16: Vending machine: Mealy to synch. Mealy
0 0 1 0
0 0 1 1
1 0 1 1
0 1 1 1
Q1
Open
Q0
N
D
0 0 1 0
0 0 1 1
X X 1 X
0 1 1 1
Q1
Open
Q0
N
D
OPEN = reset'(Q1 + D + Q0N)(Q0'N + Q0N' + Q1N + Q1D) = reset'(Q1Q0N' + Q1N + Q1D + Q0'ND + Q0N'D)
OPEN = reset’(Q1Q0 + Q1N + Q1D + Q0D)

## Slide 17: Vending machine (synch. Mealy PLD mapping)
OPEN = reset'(Q1Q0N' + Q1N + Q1D + Q0'ND + Q0N'D)
OPEN
D
Q
D
Q
D
Q
Q0
Q1
Open
Seq
Seq
Seq
CLK
N
D
Reset

## Slide 18: Example: traffic light controller
A busy highway is intersected by a little used farmroad
Detectors C sense the presence of cars waiting on the farmroad
  with no car on farmroad, light remain green in highway direction
  if vehicle on farmroad, highway lights go from Green to Yellow to Red, allowing the farmroad lights to become green
  these stay green only as long as a farmroad car is detected but never longer than a set interval
  when these are met, farm lights transition from Green to Yellow to Red, allowing highway to return to green
  even if farmroad vehicles are waiting, highway gets at least a set interval as green
Assume you have an interval timer that generates:
  a short time pulse (TS) and
  a long time pulse (TL),
  in response to a set (ST) signal.
  TS is to be used for timing yellow lights and TL for green lights

## Slide 19: Example: traffic light controller (cont’)
highway
farm road
car sensors
Highway/farm road intersection

## Slide 20: Example: traffic light controller (cont’)
Tabulation of inputs and outputs inputs description outputs description reset place FSM in initial state HG, HY, HR assert green/yellow/red highway lights C detect vehicle on the farm road FG, FY, FR assert green/yellow/red highway lights TS short time interval expired ST start timing a short or long interval TL long time interval expired
Tabulation of unique states – some light configurations imply others state description HG highway green (farm road red) HY highway yellow (farm road red) FG farm road green (highway red) FY farm road yellow (highway red)

## Slide 21: Example: traffic light controller (cont’)
State diagram
Reset
TS'
TS / ST
(TL•C)'
TL•C / ST
TS'
TS / ST
(TL+C')'
TL+C' / ST
HG
FG
FY
HY

## Slide 22: Example: traffic light controller (cont’)
Inputs Present State Next State Outputs C TL TS ST H F 0 – – HG HG 0 Green Red – 0 – HG HG 0 Green Red 1 1 – HG HY 1 Green Red – – 0 HY HY 0 Yellow Red – – 1 HY FG 1 Yellow Red 1 0 – FG FG 0 Red Green 0 – – FG FY 1 Red Green – 1 – FG FY 1 Red Green – – 0 FY FY 0 Red Yellow – – 1 FY HG 1 Red Yellow
SA1: HG = 00 HY = 01 FG = 11 FY = 10 SA2: HG = 00 HY = 10 FG = 01 FY = 11 SA3: HG = 0001 HY = 0010 FG = 0100 FY = 1000 (one-hot)
output encoding – similar problem to state assignment (Green = 00, Yellow = 01, Red = 10)
Generate state table with symbolic states
Consider state assignments

## Slide 23: Logic for different state assignments
SA1 NS1 = C•TL'•PS1•PS0 + TS•PS1'•PS0 + TS•PS1•PS0' + C'•PS1•PS0 + TL•PS1•PS0 NS0 = C•TL•PS1'•PS0' + C•TL'•PS1•PS0 + PS1'•PS0 ST = C•TL•PS1'•PS0' + TS•PS1'•PS0 + TS•PS1•PS0' + C'•PS1•PS0 + TL•PS1•PS0 H1 = PS1 H0 = PS1'•PS0 F1 = PS1' F0 = PS1•PS0‘
SA2 NS1 = C•TL•PS1' + TS'•PS1 + C'•PS1'•PS0 NS0 = TS•PS1•PS0' + PS1'•PS0 + TS'•PS1•PS0 ST = C•TL•PS1' + C'•PS1'•PS0 + TS•PS1 H1 = PS0 H0 = PS1•PS0' F1 = PS0' F0 = PS1•PS0
SA3 NS3 = C'•PS2 + TL•PS2 + TS'•PS3 NS2 = TS•PS1 + C•TL'•PS2 NS1 = C•TL•PS0 + TS'•PS1 NS0 = C'•PS0 + TL'•PS0 + TS•PS3 ST = C•TL•PS0 + TS•PS1 + C'•PS2 + TL•PS2 + TS•PS3 H1 = PS3 + PS2 H0 = PS1 F1 = PS1 + PS0 F0 = PS3

## Slide 24: Sequential logic implementation summary
Models for representing sequential circuits
  finite state machines and their state diagrams
  Mealy, Moore, and synchronous Mealy machines
Finite state machine design procedure
  deriving state diagram
  deriving state transition table
  assigning codes to states
  determining next state and output functions
  implementing combinational logic
Implementation technologies
  random logic + FFs
  PAL with FFs (programmable logic devices – PLDs)