## Slide 1: Combinational Logic Technologies
Standard gates
  gate packages
  cell libraries
Regular logic
  multiplexers
  decoders
Two-level programmable logic
  PALs
  PLAs
  ROMs

## Slide 2: Random logic
Transistors quickly integrated into logic gates (1960s)
Catalog of common gates (1970s)
  Texas Instruments Logic Data Book – the yellow bible
  all common packages listed and characterized (delays, power)
  typical packages:
    in 14-pin IC: 6-inverters, 4 NAND gates, 4 XOR gates
Today, very few parts are still in use
However, parts libraries exist for chip design
  designers reuse already characterized logic gates on chips
  same reasons as before
  difference is that the parts don’t exist in physical inventory – created as needed

## Slide 3: Random logic
Too hard to figure out exactly what gates to use
  map from logic to NAND/NOR networks
  determine minimum number of packages
    slight changes to logic function could decrease cost
Changes to difficult to realize
  need to rewire parts
  may need new parts
  design with spares (few extra inverters and gates on every board)

## Slide 4: Regular logic
Need to make design faster
Need to make engineering changes easier to make
Simpler for designers to understand and map to functionality
  harder to think in terms of specific gates
  better to think in terms of a large multi-purpose block

## Slide 5: Making connections
multiplexer
demultiplexer
4x4 switch
control
control
Direct point-to-point connections between gates
  wires we've seen so far
Route one of many inputs to a single output --- multiplexer
Route a single input to one of many outputs --- demultiplexer

## Slide 6: Mux and demux
Switch implementation of multiplexers and demultiplexers
  can be composed to make arbitrary size switching networks
  used to implement multiple-source/multiple-destination interconnections
A
B
Y
Z
A
B
Y
Z

## Slide 7: Mux and demux (cont'd)
multiple input sources
multiple output destinations
MUX
A
B
Sum
Sa
Ss
Sb
B0
MUX
DEMUX
Uses of multiplexers/demultiplexers in multi-point connections
B1
A0
A1
S0
S1

## Slide 8: Multiplexers/selectors
two alternative forms
for a 2:1 Mux truth table
functional form
logical form
A Z 0 I0 1 I1
I1 I0 A Z 0 0 0 0 0 0 1 0 0 1 0 1 0 1 1 0 1 0 0 0 1 0 1 1 1 1 0 1 1 1 1 1
Z = A' I0 + A I1
Multiplexers/selectors: general concept
  2n data inputs, n control inputs (called "selects"), 1 output
  used to connect 2n points to a single point
  control signal pattern forms binary index of input connected to output

## Slide 9: Multiplexers/selectors (cont'd)
2 -1
I0 I1 I2 I3 I4 I5 I6 I7
A B C
8:1 mux
Z
I0 I1 I2 I3
A B
4:1 mux
Z
I0 I1
A
2:1 mux
Z
k=0
n
2:1 mux: Z = A' I0 + A I1
4:1 mux: Z = A' B' I0 + A' B I1 + A B' I2 + A B I3
8:1 mux: Z = A' B' C' I0 + A' B' C I1 + A' B C' I2 + A' B C I3 + A B' C' I4 + A B' C I5 + A B C' I6 + A B C I7
In general: Z =  (mkIk)
  in minterm shorthand form for a 2n:1 Mux

## Slide 10: Gate level implementation of muxes
2:1 mux
4:1 mux

## Slide 11: Cascading multiplexers
control signals B and C simultaneously choose one of I0, I1, I2, I3 and one of I4, I5, I6, I7 control signal A chooses which of the upper or lower mux's output to gate to Z
alternative implementation
C
Z
A B
4:1 mux
2:1 mux
2:1 mux
2:1 mux
2:1 mux
I4 I5
I2 I3
I0 I1
I6 I7
8:1 mux
Large multiplexers can be implemented by cascading smaller ones
Z
I0 I1 I2 I3
A
I4 I5 I6 I7
B C
4:1 mux
4:1 mux
2:1 mux
8:1 mux

## Slide 12: Multiplexers as general-purpose logic
C
A
B
0 1 2 3 4 5 6 7
1 0 1 0 0 0 1 1
S2
8:1 MUX
S1
S0
F
A 2n:1 multiplexer can implement any function of n variables
  with the variables used as control inputs and
  the data inputs tied to 0 or 1
  in essence, a lookup table
Example:
  F(A,B,C) = m0 + m2 + m6 + m7 = A'B'C' + A'BC' + ABC' + ABC = A'B'(C') + A'B(C') + AB'(0) + AB(1)

## Slide 13: Multiplexers as general-purpose logic (cont’d)
A B C F 0 0 0 1 0 0 1 0 0 1 0 1 0 1 1 0 1 0 0 0 1 0 1 0 1 1 0 1 1 1 1 1
C' C' 0 1
A
B
S1
S0
F
0 1 2 3
4:1 MUX
C' C' 0 1
F
C
A
B
0 1 2 3 4 5 6 7
1 0 1 0 0 0 1 1
S2
8:1 MUX
S1
S0
A 2n-1:1 multiplexer can implement any function of n variables
  with n-1 variables used as control inputs and
  the data inputs tied to the last variable or its complement
Example:
  F(A,B,C) = m0 + m2 + m6 + m7 = A'B'C' + A'BC' + ABC' + ABC = A'B'(C') + A'B(C') + AB'(0) + AB(1)

## Slide 14: Multiplexers as general-purpose logic (cont’d)
n-1 mux control variables
  single mux data variable
four possible
configurations of truth table rows can be expressed as a function of In
choose A,B,C as control variables multiplexer implementation
I0 I1 . . . In-1 In F . . . . 0 0 0 1 1 . . . . 1 0 1 0 1 0 In In' 1
Generalization
Example: G(A,B,C,D) can be implemented by an 8:1 MUX
C
A
B
0 1 2 3 4 5 6 7
1 D 0 1 D’ D D’ D’
S2
8:1 MUX
S1
S0
A B C D G 0 0 0 0 1 0 0 0 1 1 0 0 1 0 0 0 0 1 1 1 0 1 0 0 0 0 1 0 1 0 0 1 1 0 1 0 1 1 1 1 1 0 0 0 1 1 0 0 1 0 1 0 1 0 0 1 0 1 1 1 1 1 0 0 1 1 1 0 1 0 1 1 1 0 1 1 1 1 1 0
1
D 0 1
D' D D’ D’

## Slide 15: Activity
Map the following equation to an 4:1 multiplexer using a minimum of external gates:
A B C D Z 0 0 0 0 0 0 0 0 1 0 0 0 1 0 1 0 0 1 1 0 0 1 0 0 0 0 1 0 1 0 0 1 1 0 1 0 1 1 1 1 1 0 0 0 0 1 0 0 1 0 1 0 1 0 1 1 0 1 1 0 1 1 0 0 1 1 1 0 1 1 1 1 1 0 1 1 1 1 1 1
0 when B’C’
D’ when B’C
A when BC’
1 when BC
Z = B’C’(0) + B’C(D’) + BC’(A) + BC(1)
B
C
S1
S0
F
0 1 2 3
4:1 MUX
0 D’ A 1

## Slide 16: Demultiplexers/decoders
1:2 Decoder:
O0 = G  S’
O1 = G  S
2:4 Decoder:
O0 = G  S1’  S0’
O1 = G  S1’  S0
O2 = G  S1  S0’
O3 = G  S1  S0
3:8 Decoder:
O0 = G  S2’  S1’  S0’
O1 = G  S2’  S1’  S0
O2 = G  S2’  S1  S0’
O3 = G  S2’  S1  S0
O4 = G  S2  S1’  S0’
O5 = G  S2  S1’  S0
O6 = G  S2  S1  S0’
O7 = G  S2  S1  S0
Decoders/demultiplexers: general concept
  single data input, n control inputs, 2n outputs
  control inputs (called “selects” (S)) represent binary index of output to which the input is connected
  data input usually called “enable” (G)

## Slide 17: Gate level implementation of demultiplexers
active-high enable
active-low enable
active-high enable
active-low enable
O0
G
S
O1
O0
\G
S
O1
S1
O2
O3
O0
G
O1
S0
S1
O2
O3
O0
\G
O1
S0
1:2 decoders
2:4 decoders

## Slide 18: Demultiplexers as general-purpose logic
demultiplexer generates appropriate
minterm based on control signals
(it "decodes" control signals)
A n:2n decoder can implement any function of n variables
  with the variables used as control inputs
  the enable inputs tied to 1 and
  the appropriate minterms summed to form the function
A'B'C' A'B'C A'BC' A'BC AB'C' AB'C ABC' ABC
C
A
B
0 1 2 3 4 5 6 7
S2
3:8 DEC
S1
S0
“1”

## Slide 19: Demultiplexers as general-purpose logic (cont’d)
F1
F2
F3
F1 = A' B C' D + A' B' C D + A B C D
F2 = A B C' D’ + A B C
F3 = (A' + B' + C' + D')
A
B
0 A'B'C'D' 1 A'B'C'D 2 A'B'CD' 3 A'B'CD 4 A'BC'D' 5 A'BC'D 6 A'BCD' 7 A'BCD 8 AB'C'D' 9 AB'C'D 10 AB'CD' 11 AB'CD 12 ABC'D' 13 ABC'D 14 ABCD' 15 ABCD
4:16 DEC
Enable
C
D

## Slide 20: Cascading decoders
0 A'B'C'D'E' 1 2 3 4 5 6 7
S2
3:8 DEC
S1
S0
A
B
0 1 2 3
S1
2:4 DEC
S0
F
0 1 2 A'BC'DE' 3 4 5 6 7
S2
3:8 DEC
S1
S0
E
C
D
0 AB'C'D'E' 1 2 3 4 5 6 7 AB'CDE
5:32 decoder
  1x2:4 decoder
  4x3:8 decoders
3:8 DEC
0 1 2 3 4 5 6 7 ABCDE
E
C
D
S2
S1
S0
S2
3:8 DEC
S1
S0

## Slide 21: Programmable logic arrays
• • •
inputs
AND array
• • •
outputs
OR array
product terms
Pre-fabricated building block of many AND/OR gates
  actually NOR or NAND
  "personalized" by making or breaking connections among the gates
  programmable array block diagram for sum of products form

## Slide 22: Enabling concept
example:
F0 = A + B' C'
F1 = A C' + A B
F2 = B' C' + A B
F3 = B' C + A
personality matrix
1 = uncomplemented in term
0 = complemented in term
– = does not participate
1 = term connected to output
0 = no connection to output
input side:
output side:
product inputs outputs
term A B C F0 F1 F2 F3 AB 1 1 – 0 1 1 0 B'C – 0 1 0 0 0 1 AC' 1 – 0 0 1 0 0 B'C' – 0 0 1 0 1 0 A 1 – – 1 0 0 1
reuse of terms
Shared product terms among outputs

## Slide 23: Before programming
All possible connections are available before "programming"
  in reality, all AND and OR gates are NANDs

## Slide 24: After programming
A
B
C
F1
F2
F3
F0
AB
B'C
AC'
B'C'
A
Unwanted connections are "blown"
  fuse (normally connected, break unwanted ones)
  anti-fuse (normally disconnected, make wanted connections)

## Slide 25: Alternate representation for high fan-in structures
notation for implementing
F0 = A B + A' B'
F1 = C D' + C' D
AB+A'B'
CD'+C'D
AB
A'B'
CD'
C'D
A
B
C
D
Short-hand notation so we don't have to draw all the wires
  signifies a connection is present and perpendicular signal is an input to gate

## Slide 26: Programmable logic array example
A B C F1 F2 F3 F4 F5 F6
0 0 0 0 0 1 1 0 0
0 0 1 0 1 0 1 1 1
0 1 0 0 1 0 1 1 1
0 1 1 0 1 0 1 0 0
1 0 0 0 1 0 1 1 1
1 0 1 0 1 0 1 0 0
1 1 0 0 1 0 1 0 0
1 1 1 1 1 0 0 1 1
A'B'C'
A'B'C
A'BC'
A'BC
AB'C'
AB'C
ABC'
ABC
A
B
C
F1
F2
F3
F4
F5
F6
full decoder as for memory address
bits stored in memory
Multiple functions of A, B, C
  F1 = A B C
  F2 = A + B + C
  F3 = A' B' C'
  F4 = A' + B' + C'
  F5 = A xor B xor C
  F6 = A xnor B xnor C

## Slide 27: PALs and PLAs
a given column of the OR array has access to only a subset of the possible product terms
Programmable logic array (PLA)
  what we've seen so far
  unconstrained fully-general AND and OR arrays
Programmable array logic (PAL)
  constrained topology of the OR array
  innovation by Monolithic Memories
  faster and smaller OR plane

## Slide 28: PALs and PLAs: design example
minimized functions:
W = A + B D + B C
X = B C'
Y = B + C
Z = A'B'C'D + B C D + A D' + B' C D'
A B C D W X Y Z 0 0 0 0 0 0 0 0 0 0 0 1 0 0 0 1 0 0 1 0 0 0 1 1 0 0 1 1 0 0 1 0 0 1 0 0 0 1 1 0 0 1 0 1 1 1 1 0 0 1 1 0 1 0 1 0 0 1 1 1 1 0 1 1 1 0 0 0 1 0 0 1 1 0 0 1 1 0 0 0 1 0 1 – – – – – 1 1 – – – – – –
BCD to Gray code converter

## Slide 29: PALs and PLAs: design example (cont’d)
not a particularly good
candidate for PAL/PLA
implementation since no terms are shared among outputs
however, much more compact and regular implementation when compared with discrete AND and OR gates
A B C D
minimized functions:
W = A + B D + B C
X = B C'
Y = B + C
Z = A'B'C'D + B C D + A D' + B' C D'
Code converter: programmed PLA
A
BD
BC
BC'
B
C
A'B'C'D
BCD
AD'
BCD'
W X Y Z

## Slide 30: PALs and PLAs: design example (cont’d)
4 product terms per each OR gate
A
BD
BC
0
BC'
0
0
0
B
C
0
0
A'B'C'D
BCD
AD'
B'CD'
W X Y Z
A B C D
Code converter: programmed PAL

## Slide 31: PALs and PLAs: design example (cont’d)
W
X
Y
Z
B
B
B
B
B
B
\B
C
C
C
C
C
A
A
A
D
D
D
\D
\D
Code converter: NAND gate implementation
  loss or regularity, harder to understand
  harder to make changes

## Slide 32: PALs and PLAs: another design example
EQ NE LT GT
A'B'C'D'
A'BC'D
ABCD
AB'CD'
AC'
A'C
B'D
BD'
A'B'D
B'CD
ABC
BC'D'
A B C D
Magnitude comparator
A B C D EQ NE LT GT 0 0 0 0 1 0 0 0 0 0 0 1 0 1 1 0 0 0 1 0 0 1 1 0 0 0 1 1 0 1 1 0 0 1 0 0 0 1 0 1 0 1 0 1 1 0 0 0 0 1 1 0 0 1 1 0 0 1 1 1 0 1 1 0 1 0 0 0 0 1 0 1 1 0 0 1 0 1 0 1 1 0 1 0 1 0 0 0 1 0 1 1 0 1 1 0 1 1 0 0 0 1 0 1 1 1 0 1 0 1 0 1 1 1 1 0 0 1 0 1 1 1 1 1 1 0 0 0
minimized functions:
EQ = A’B’C’D’ + A’BC’D + ABCD + AB’CD’ NE = AC’ + A’C + B’D + BD’
LT = A’C + A’B’D + B’CD GT = AC’ + ABC + BC’D’

## Slide 33: Activity
Map the following functions to the PLA below:
  W = AB + A’C’ + BC’
  X = ABC + AB’ + A’B
  Y = ABC’ + BC + B’C’
A
B
C
W
X
Y

## Slide 34: Activity (cont’d)
9 terms won’t fit in a 7 term PLA
  can apply concensus theorem to W to simplify to: W = AB + A’C’
8 terms wont’ fit in a 7 term PLA
  observe that AB = ABC + ABC’
  can rewrite W to reuse terms: W = ABC + ABC’ + A’C’
Now it fits
  W = ABC + ABC’ + A’C’
  X = ABC + AB’ + A’B
  Y = ABC’ + BC + B’C’
This is called technology mapping
  manipulating logic functions so that they can use available resources
ABC
ABC’
A’C’
AB’
A’B
BC
B’C’
A
B
C
W
X
Y

## Slide 35: Read-only memories
decoder
0 n-1
  Address
2 -1
n
0
1
1
1
1
word[i] = 0011 word[j] = 1010
bit lines (normally pulled to 1 through resistor – selectively connected to 0 by word line controlled switches)
j
i
internal organization
word lines (only one is active – decoder is just right for this)
Two dimensional array of 1s and 0s
  entry (row) is called a "word"
  width of row = word-size
  index is called an "address"
  address is input
  selected word is output

## Slide 36: ROMs and combinational logic
F0 = A' B' C + A B' C' + A B' C
F1 = A' B' C + A' B C' + A B C
F2 = A' B' C' + A' B' C + A B' C'
F3 = A' B C + A B' C' + A B C'
truth table
A B C F0 F1 F2 F3
0 0 0 0 0 1 0 0 0 1 1 1 1 0 0 1 0 0 1 0 0 0 1 1 0 0 0 1
1 0 0 1 0 1 1
1 0 1 1 0 0 0
1 1 0 0 0 0 1
1 1 1 0 1 0 0
block diagram
ROM 8 words x 4 bits/word
address
outputs
A B C F0 F1 F2 F3
Combinational logic implementation (two-level canonical form) using a ROM

## Slide 37: ROM structure
Similar to a PLA structure but with a fully decoded AND array
  completely flexible OR array (unlike PAL)
n address lines
• • •
inputs
decoder
2n word lines
• • •
outputs
memory array (2n words by m bits)
m data lines

## Slide 38: ROM vs. PLA
ROM approach advantageous when
  design time is short (no need to minimize output functions)
  most input combinations are needed (e.g., code converters)
  little sharing of product terms among output functions
ROM problems
  size doubles for each additional input
  can't exploit don't cares
PLA approach advantageous when
  design tools are available for multi-output minimization
  there are relatively few unique minterm combinations
  many minterms are shared among the output functions
PAL problems
  constrained fan-ins on OR plane

## Slide 39: Regular logic structures for two-level logic
ROM – full AND plane, general OR plane
  cheap (high-volume component)
  can implement any function of n inputs
  medium speed
PAL – programmable AND plane, fixed OR plane
  intermediate cost
  can implement functions limited by number of terms
  high speed (only one programmable plane that is much smaller than ROM's decoder)
PLA – programmable AND and OR planes
  most expensive (most complex in design, need more sophisticated tools)
  can implement any function up to a product term limit
  slow (two programmable planes)

## Slide 40: Regular logic structures for multi-level logic
Difficult to devise a regular structure for arbitrary connections between a large set of different types of gates
  efficiency/speed concerns for such a structure
  in 467 you'll learn about field programmable gate arrays (FPGAs) that are just such programmable multi-level structures
    programmable multiplexers for wiring
    lookup tables for logic functions (programming fills in the table)
    multi-purpose cells (utilization is the big issue)
Use multiple levels of PALs/PLAs/ROMs
  output intermediate result
  make it an input to be used in further logic

## Slide 41: Combinational logic technology summary
Random logic
  Single gates or in groups
  conversion to NAND-NAND and NOR-NOR networks
  transition from simple gates to more complex gate building blocks
  reduced gate count, fan-ins, potentially faster
  more levels, harder to design
Time response in combinational networks
  gate delays and timing waveforms
  hazards/glitches (what they are and why they happen)
Regular logic
  multiplexers/decoders
  ROMs
  PLAs/PALs
  advantages/disadvantages of each