## Slide 1: Combinational logic design case studies
General design procedure
Case studies
  BCD to 7-segment display controller
  logical function unit
  process line controller
  calendar subsystem
Arithmetic circuits
  integer representations
  addition/subtraction
  arithmetic/logic units

## Slide 2: General design procedure for combinational logic
1. Understand the problem
  what is the circuit supposed to do?
  write down inputs (data, control) and outputs
  draw block diagram or other picture
2. Formulate the problem using a suitable design representation
  truth table or waveform diagram are typical
  may require encoding of symbolic inputs and outputs
3. Choose implementation target
  ROM, PAL, PLA
  mux, decoder and OR-gate
  discrete gates
4. Follow implementation procedure
  K-maps for two-level, multi-level
  design tools and hardware description language (e.g., Verilog)

## Slide 3: BCD to 7-segment display controller
BCD to 7–segment control signal decoder
c0 c1 c2 c3 c4 c5 c6
A B C D
Understanding the problem
  input is a 4 bit bcd digit (A, B, C, D)
  output is the control signals for the display (7 outputs C0 – C6)
Block diagram
c1
c5
c2
c4
c6
c0
c3

## Slide 4: Formalize the problem
A B C D C0 C1 C2 C3 C4 C5 C6
0 0 0 0 1 1 1 1 1 1 0
0 0 0 1 0 1 1 0 0 0 0
0 0 1 0 1 1 0 1 1 0 1
0 0 1 1 1 1 1 1 0 0 1
0 1 0 0 0 1 1 0 0 1 1
0 1 0 1 1 0 1 1 0 1 1
0 1 1 0 1 0 1 1 1 1 1
0 1 1 1 1 1 1 0 0 0 0
1 0 0 0 1 1 1 1 1 1 1
1 0 0 1 1 1 1 0 0 1 1
1 0 1 – – – – – – – –
1 1 – – – – – – – – –
Truth table
  show don't cares
Choose implementation target
  if ROM, we are done
  don't cares imply PAL/PLA may be attractive
Follow implementation procedure
  minimization using K-maps

## Slide 5: Implementation as minimized sum-of-products
C0 = A + B D + C + B' D'
C1 = C' D' + C D + B'
C2 = B + C' + D
C3 = B' D' + C D' + B C' D + B' C
C4 = B' D' + C D'
C5 = A + C' D' + B D' + B C'
C6 = A + C D' + B C' + B' C
15 unique product terms when minimized individually
1 0 X 1
0 1 X 1 1 1 X X
1 1 X X
D
A
B
C
1 1 X 1
1 0 X 1 1 1 X X
1 0 X X
D
A
B
C
0 1 X 1
0 1 X 1 1 0 X X
1 1 X X
D
A
B
C
1 1 X 1
1 1 X 1 1 1 X X
0 1 X X
D
A
B
C
1 0 X 1
0 1 X 0 1 0 X X
1 1 X X
D
A
B
C
1 0 X 1
0 0 X 0 0 0 X X
1 1 X X
D
A
B
C
1 1 X 1
0 1 X 1 0 0 X X
0 1 X X
D
A
B
C

## Slide 6: Implementation as minimized S-o-P (cont'd)
C0 = B C' D + C D + B' D' + B C D' + A C1 = B' D + C' D' + C D + B' D' C2 = B' D + B C' D + C' D' + C D + B C D' C3 = B C' D + B' D + B' D' + B C D' C4 = B' D' + B C D' C5 = B C' D + C' D' + A + B C D' C6 = B' C + B C' + B C D' + A
C0 = A + B D + C + B' D'
C1 = C' D' + C D + B'
C2 = B + C' + D
C3 = B' D' + C D' + B C' D + B' C
C4 = B' D' + C D'
C5 = A + C' D' + B D' + B C'
C6 = A + C D' + B C' + B' C
C2
Can do better
  9 unique product terms (instead of 15)
  share terms among outputs
  each output not necessarily in minimized form
1 1 X 1
1 1 X 1 1 1 X X
0 1 X X
D
A
B
C
1 1 X 1
1 1 X 1 1 1 X X
0 1 X X
D
A
B
C
C2

## Slide 7: PLA implementation
BC'
B'C
B'D
BC'D
C'D'
CD
B'D'
A
BCD'
A B C D
C0 C1 C2 C3 C4 C5 C6 C7

## Slide 8: PAL implementation/Discrete gate implementation
C0 = C3 + A' B X' + A D Y
C1 = Y + A' C5' + C' D' C6
C2 = C5 + A' B' D + A' C D
C3 = C4 + B D C5 + A' B' X'
C4 = D' Y + A' C D'
C5 = C' C4 + A Y + A' B X
C6 = A C4 + C C5 + C4' C5 + A' B' C
X = C' + D'
Y = B' C'
C2 = B + C' + D
C2 = B' D + B C' D + C' D' + C D + B C D'
C2 = B' D + B C' D + C' D' + W
W = C D + B C D'
Limit of 4 product terms per output
  decomposition of functions with larger number of terms
  do not share terms in PAL anyway (although there are some with some shared terms)
decompose into multi-level logic (hopefully with CAD support)
  find common sub-expressions among functions
need another input and another output

## Slide 9: Logical function unit
C0 C1 C2 Function Comments 0 0 0 1 always 1 0 0 1 A + B logical OR 0 1 0 (A • B)' logical NAND 0 1 1 A xor B logical xor 1 0 0 A xnor B logical xnor 1 0 1 A • B logical AND 1 1 0 (A + B)' logical NOR 1 1 1 0 always 0
3 control inputs: C0, C1, C2 2 data inputs: A, B 1 output: F
Multi-purpose function block
  3 control inputs to specify operation to perform on operands
  2 data inputs for operands
  1 output of the same bit-width as operands

## Slide 10: Formalize the problem
choose implementation technology 5-variable K-map to discrete gates multiplexor implementation
1 0
A B
A B
A B
C0 C1 C2 A B F
0 0 0 0 0 1
0 0 0 0 1 1
0 0 0 1 0 1
0 0 0 1 1 1
0 0 1 0 0 0
0 0 1 0 1 1
0 0 1 1 0 1
0 0 1 1 1 1
0 1 0 0 0 1
0 1 0 0 1 1
0 1 0 1 0 1
0 1 0 1 1 0
0 1 1 0 0 0
0 1 1 0 1 1
0 1 1 1 0 1
0 1 1 1 1 0
1 0 0 0 0 1
1 0 0 0 1 0
1 0 0 1 0 0
1 0 0 1 1 1
1 0 1 0 0 0
1 0 1 0 1 0
1 0 1 1 0 0
1 0 1 1 1 1
1 1 0 0 0 1
1 1 0 0 1 0
1 1 0 1 0 0
1 1 0 1 1 0
1 1 1 0 0 0
1 1 1 0 1 0
1 1 1 1 0 0
1 1 1 1 1 0
C2
C0
C1
0 1 2 3 4 5 6 7
S2
8:1 MUX
S1
S0
F

## Slide 11: Production line control
Rods of varying length (+/-10%) travel on conveyor belt
  mechanical arm pushes rods within spec (+/-5%) to one side
  second arm pushes rods too long to other side
  rods that are too short stay on belt
  3 light barriers (light source + photocell) as sensors
  design combinational logic to activate the arms
Understanding the problem
  inputs are three sensors
  outputs are two arm control signals
  assume sensor reads "1" when tripped, "0" otherwise
  call sensors A, B, C

## Slide 12: Sketch of problem
Position of sensors
  A to B distance = specification – 5%
  A to C distance = specification + 5%
Within Spec
Too Short
Too Long
A
B
C
spec - 5%
spec + 5%

## Slide 13: Formalize the problem
logic implementation now straightforward just use three 3-input AND gates "too short" = AB'C' (only first sensor tripped) "in spec" = A B C' (first two sensors tripped)
"too long" = A B C (all three sensors tripped)
A B C Function 0 0 0 do nothing 0 0 1 do nothing 0 1 0 do nothing 0 1 1 do nothing 1 0 0 too short 1 0 1 don't care 1 1 0 in spec 1 1 1 too long
Truth table
  show don't cares

## Slide 14: Calendar subsystem
integer number_of_days ( month, leap_year_flag) {
  switch (month) {
    case 1: return (31);
    case 2: if (leap_year_flag == 1)
    then return (29) else return (28);
    case 3: return (31);
    case 4: return (30);
    case 5: return (31);
    case 6: return (30);
    case 7: return (31);
    case 8: return (31);
    case 9: return (30);
    case 10: return (31);
    case 11: return (30);
    case 12: return (31);
    default: return (0);
  }
}
Determine number of days in a month (to control watch display)
  used in controlling the display of a wrist-watch LCD screen
  inputs: month, leap year flag
  outputs: number of days
Use software implementation to help understand the problem

## Slide 15: Formalize the problem
leap
month
28
29
30
31
month leap 28 29 30 31 0000 – – – – – 0001 – 0 0 0 1 0010 0 1 0 0 0 0010 1 0 1 0 0 0011 – 0 0 0 1 0100 – 0 0 1 0 0101 – 0 0 0 1 0110 – 0 0 1 0 0111 – 0 0 0 1 1000 – 0 0 0 1 1001 – 0 0 1 0 1010 – 0 0 0 1 1011 – 0 0 1 0 1100 – 0 0 0 1 1101 – – – – – 111– – – – – –
Encoding:
  binary number for month: 4 bits
  4 wires for 28, 29, 30, and 31 one-hot – only one true at any time
Block diagram:

## Slide 16: Choose implementation target and perform mapping
month leap 28 29 30 31 0000 – – – – – 0001 – 0 0 0 1 0010 0 1 0 0 0 0010 1 0 1 0 0 0011 – 0 0 0 1 0100 – 0 0 1 0 0101 – 0 0 0 1 0110 – 0 0 1 0 0111 – 0 0 0 1 1000 – 0 0 0 1 1001 – 0 0 1 0 1010 – 0 0 0 1 1011 – 0 0 1 0 1100 – 0 0 0 1 1101 – – – – – 111– – – – – –
Discrete gates
  28 =
  29 =
  30 =
  31 =
Can translate to S-o-P or P-o-S
m8’ m4’ m2 m1’ leap’
m8’ m4’ m2 m1’ leap
m8’ m4 m1’ + m8 m1
m8’ m1 + m8 m1’

## Slide 17: Leap year flag
Determine value of leap year flag given the year
  For years after 1582 (Gregorian calendar reformation),
  leap years are all the years divisible by 4,
  except that years divisible by 100 are not leap years,
  but years divisible by 400 are leap years.
Encoding the year:
  binary – easy for divisible by 4, but difficult for 100 and 400 (not powers of 2)
  BCD – easy for 100, but more difficult for 4, what about 400?
Parts:
  construct a circuit that determines if the year is divisible by 4
  construct a circuit that determines if the year is divisible by 100
  construct a circuit that determines if the year is divisible by 400
  combine the results of the previous three steps to yield the leap year flag

## Slide 18: Activity: divisible-by-4 circuit
BCD coded year
  YM8 YM4 YM2 YM1 – YH8 YH4 YH2 YH1 – YT8 YT4 YT2 YT1 – YO8 YO4 YO2 YO1
Only need to look at low-order two digits of the year all years ending in 00, 04, 08, 12, 16, 20, etc. are divisible by 4
  if tens digit is even, then divisible by 4 if ones digit is 0, 4, or 8
  if tens digit is odd, then divisible by 4 if the ones digit is 2 or 6.
Translates into the following Boolean expression (where YT1 is the year's tens digit low-order bit, YO8 is the high-order bit of year's ones digit, etc.): YT1’ (YO8’ YO4’ YO2’ YO1’ + YO8’ YO4 YO2’ YO1’ + YO8 YO4’ YO2’ YO1’ ) + YT1 (YO8’ YO4’ YO2 YO1’ + YO8’ YO4 YO2 YO1’ )
Digits with values of 10 to 15 will never occur, simplify further to yield: YT1’ YO2’ YO1’ + YT1 YO2 YO1’

## Slide 19: Divisible-by-100 and divisible-by-400 circuits
Divisible-by-100 just requires checking that all bits of two low-order digits are all 0: YT8’ YT4’ YT2’ YT1’ • YO8’ YO4’ YO2’ YO1’
Divisible-by-400 combines the divisible-by-4 (applied to the thousands and hundreds digits) and divisible-by-100 circuits (YM1’ YH2’ YH1’ + YM1 YH2 YH1’) • (YT8’ YT4’ YT2’ YT1’ • YO8’ YO4’ YO2’ YO1’ )

## Slide 20: Combining to determine leap year flag
Label results of previous three circuits: D4, D100, and D400 leap_year_flag = D4 (D100 • D400’ ) ’ = D4 • D100’ + D4 • D400 = D4 • D100’ + D400

## Slide 21: Implementation of leap year flag

## Slide 22: Arithmetic circuits
Excellent examples of combinational logic design
Time vs. space trade-offs
  doing things fast may require more logic and thus more space
  example: carry lookahead logic
Arithmetic and logic units
  general-purpose building blocks
  critical components of processor datapaths
  used within most computer instructions

## Slide 23: Number systems
Representation of positive numbers is the same in most systems
Major differences are in how negative numbers are represented
Representation of negative numbers come in three major schemes
  sign and magnitude
  1s complement
  2s complement
Assumptions
  we'll assume a 4 bit machine word
  16 different values can be represented
  roughly half are positive, half are negative

## Slide 24: Sign and magnitude
0000
0111
0011
1011
1111
1110
1101
1100
1010
1001
1000
0110
0101
0100
0010
0001
+0
+1
+2
+3
+4
+5
+6
+7
–0
–1
–2
–3
–4
–5
–6
–7
0 100 = + 4 1 100 = – 4
One bit dedicate to sign (positive or negative)
  sign: 0 = positive (or zero), 1 = negative
Rest represent the absolute value or magnitude
  three low order bits: 0 (000) thru 7 (111)
Range for n bits
  +/– 2n–1 –1 (two representations for 0)
Cumbersome addition/subtraction
  must compare magnitudes to determine sign of result

## Slide 25: 1s complement
2 = 10000
1 = 00001
2 –1 = 1111
7 = 0111
1000 = –7 in 1s complement form
4
4
If N is a positive number, then the negative of N ( its 1s complement or N' ) is N' = (2n– 1) – N
  example: 1s complement of 7
  shortcut: simply compute bit-wise complement ( 0111 -> 1000 )

## Slide 26: 1s complement (cont'd)
0000
0111
0011
1011
1111
1110
1101
1100
1010
1001
1000
0110
0101
0100
0010
0001
+0
+1
+2
+3
+4
+5
+6
+7
–7
–6
–5
–4
–3
–2
–1
–0
0 100 = + 4 1 011 = – 4
Subtraction implemented by 1s complement and then addition
Two representations of 0
  causes some complexities in addition
High-order bit can act as sign bit

## Slide 27: 2s complement
0 100 = + 4 1 100 = – 4
+0
+1
+2
+3
+4
+5
+6
+7
–8
–7
–6
–5
–4
–3
–2
–1
0000
0111
0011
1011
1111
1110
1101
1100
1010
1001
1000
0110
0101
0100
0010
0001
1s complement with negative numbers shifted one position clockwise
  only one representation for 0
  one more negative number than positive number
  high-order bit can act as sign bit

## Slide 28: 2s complement (cont’d)
2 = 10000
7 = 0111
1001 = repr. of –7
4
2 = 10000
–7 = 1001
0111 = repr. of 7
4
subtract
subtract
If N is a positive number, then the negative of N ( its 2s complement or N* ) is N* = 2n – N
  example: 2s complement of 7
  example: 2s complement of –7
  shortcut: 2s complement = bit-wise complement + 1
    0111 -> 1000 + 1 -> 1001 (representation of -7)
    1001 -> 0110 + 1 -> 0111 (representation of 7)

## Slide 29: 2s complement addition and subtraction
4
+ 3
7
0100
0011
0111
– 4
+ (– 3)
– 7
1100
1101
11001
4
– 3
1
0100
1101
10001
– 4
+ 3
– 1
1100
0011
1111
Simple addition and subtraction
  simple scheme makes 2s complement the virtually unanimous choice for integer number systems in computers

## Slide 30: Why can the carry-out be ignored?
Can't ignore it completely
  needed to check for overflow (see next two slides)
When there is no overflow, carry-out may be true but can be ignored – M + N when N > M: M* + N = (2n – M) + N = 2n + (N – M) ignoring carry-out is just like subtracting 2n – M + – N where N + M  2n–1 (– M) + (– N) = M* + N* = (2n– M) + (2n– N) = 2n – (M + N) + 2n ignoring the carry, it is just the 2s complement representation for – (M + N)

## Slide 31: Overflow in 2s complement addition/subtraction
5 + 3 = –8
–7 – 2 = +7
+0
+1
+2
+3
+4
+5
+6
+7
–8
–7
–6
–5
–4
–3
–2
–1
0000
0111
0011
1011
1111
1110
1101
1100
1010
1001
1000
0110
0101
0100
0010
0001
+0
+1
+2
+3
+4
+5
+6
+7
–8
–7
–6
–5
–4
–3
–2
–1
0000
0111
0011
1011
1111
1110
1101
1100
1010
1001
1000
0110
0101
0100
0010
0001
Overflow conditions
  add two positive numbers to get a negative number
  add two negative numbers to get a positive number

## Slide 32: Overflow conditions
5
3
– 8
0 1 1 1 0 1 0 1 0 0 1 1 1 0 0 0
– 7
– 2
7
1 0 0 0 1 0 0 1 1 1 1 0 1 0 1 1 1
5
2
7
0 0 0 0 0 1 0 1 0 0 1 0 0 1 1 1
– 3
– 5
– 8
1 1 1 1 1 1 0 1 1 0 1 1 1 1 0 0 0
overflow
overflow
no overflow
no overflow
Overflow when carry into sign bit position is not equal to carry-out

## Slide 33: Circuits for binary addition
Ai Bi Sum Cout 0 0 0 0 0 1 1 0 1 0 1 0 1 1 1 1
Ai Bi Cin Sum Cout 0 0 0 0 0 0 0 1 1 0 0 1 0 1 0 0 1 1 0 1 1 0 0 1 0 1 0 1 0 1 1 1 0 0 1 1 1 1 1 1
Half adder (add 2 1-bit numbers)
  Sum = Ai' Bi + Ai Bi' = Ai xor Bi
  Cout = Ai Bi
Full adder (carry-in to cascade for multi-bit adders)
  Sum = Ci xor A xor B
  Cout = B Ci + A Ci + A B = Ci (A + B) + A B

## Slide 34: Full adder implementations
Cout = A B + Cin (A xor B) = A B + B Cin + A Cin
A
B
Cin
S
A
A
B
B
Cin
Cout
A
B
A xor B
Cin
A xor B xor Cin
Half Adder
Sum
Cout
Cin (A xor B)
A B
Sum
Cout
Half Adder
Sum
Cout
Standard approach
  6 gates
  2 XORs, 2 ANDs, 2 ORs
Alternative implementation
  5 gates
  half adder is an XOR gate and AND gate
  2 XORs, 2 ANDs, 1 OR

## Slide 35: Adder/subtractor
A
B
Cout
Sum
Cin
0
1
Add' Subtract
A0
B0
B0'
Sel
Overflow
A
B
Cout
Sum
Cin
A1
B1
B1'
Sel
A
B
Cout
Sum
Cin
A2
B2
B2'
Sel
0
1
0
1
0
1
A
B
Cout
Sum
Cin
A3
B3
B3'
Sel
S3
S2
S1
S0
Use an adder to do subtraction thanks to 2s complement representation
  A – B = A + (– B) = A + B' + 1
  control signal selects B or 2s complement of B

## Slide 36: Ripple-carry adders
A
A
B
B
Cin
Cout
@0
@0
@0
@0
@N
@1
@1
@N+1
@N+2
late
arriving
signal
two gate delays
to compute Cout
4 stage
adder
A0
B0
0
S0 @2
A1
B1
C1 @2
S1 @3
A2
B2
C2 @4
S2 @5
A3
B3
C3 @6
S3 @7
Cout @8
Critical delay
  the propagation of carry from low to high order stages

## Slide 37: Ripple-carry adders (cont’d)
Critical delay
  the propagation of carry from low to high order stages
  1111 + 0001 is the worst case addition
  carry must propagate through all bits

## Slide 38: Carry-lookahead logic
Carry generate: Gi = Ai Bi
  must generate carry when A = B = 1
Carry propagate: Pi = Ai xor Bi
  carry-in will equal carry-out here
Sum and Cout can be re-expressed in terms of generate/propagate:
  Si = Ai xor Bi xor Ci = Pi xor Ci
  Ci+1 = Ai Bi + Ai Ci + Bi Ci = Ai Bi + Ci (Ai + Bi) = Ai Bi + Ci (Ai xor Bi) = Gi + Ci Pi

## Slide 39: Carry-lookahead logic (cont’d)
Re-express the carry logic as follows:
  C1 = G0 + P0 C0
  C2 = G1 + P1 C1 = G1 + P1 G0 + P1 P0 C0
  C3 = G2 + P2 C2 = G2 + P2 G1 + P2 P1 G0 + P2 P1 P0 C0
  C4 = G3 + P3 C3 = G3 + P3 G2 + P3 P2 G1 + P3 P2 P1 G0 + P3 P2 P1 P0 C0
Each of the carry equations can be implemented with two-level logic
  all inputs are now directly derived from data inputs and not from intermediate carries
  this allows computation of all sum outputs to proceed in parallel

## Slide 40: Carry-lookahead implementation
G3
C0
C0
C0
C0
P0
P0
P0
P0
G0
G0
G0
G0
C1 @ 3
P1
P1
P1
P1
P1
P1
G1
G1
G1
C2 @ 3
P2
P2
P2
P2
P2
P2
G2
G2
C3 @ 3
P3
P3
P3
P3
C4 @ 3
Pi @ 1 gate delay
Ci
Si @ 2 gate delays
Bi
Ai
Gi @ 1 gate delay
increasingly complex logic for carries
Adder with propagate and generate outputs

## Slide 41: Carry-lookahead implementation (cont’d)
A0
B0
0
S0 @2
A1
B1
C1 @2
S1 @3
A2
B2
C2 @4
S2 @5
A3
B3
C3 @6
S3 @7
Cout @8
A0
B0
0
S0 @2
A1
B1
C1 @3
S1 @4
A2
B2
C2 @3
S2 @4
A3
B3
C3 @3
S3 @4
C4 @3
C4 @3
Carry-lookahead logic generates individual carries
  sums computed much more quickly in parallel
  however, cost of carry logic increases with more stages

## Slide 42: Carry-lookahead adder with cascaded carry-lookahead logic
Lookahead Carry Unit
C0
P0
G0
P1
G1
P2
G2
P3
G3
C3
C2
C1
C0
P3-0
G3-0
C4
@3
@2
@4
@3
@2
@5
@3
@2
@5
@3
@2
@4
@5
@3
@0
C16
A[15-12]
B[15-12]
C12
S[15-12]
A[11-8]
B[11-8]
C8
S[11-8]
A[7-4]
B[7-4]
C4
S[7-4]
@7
@8
@8
A[3-0]
B[3-0]
C0
S[3-0]
@0
@4
4
4
4
P
G
4-bit Adder
4
4
4
P
G
4-bit Adder
4
4
4
P
G
4-bit Adder
4
4
4
P
G
4-bit Adder
Carry-lookahead adder
  4 four-bit adders with internal carry lookahead
  second level carry lookahead unit extends lookahead to 16 bits
G = G3 + P3 G2 + P3 P2 G1 + P3 P2 P1 G0
P = P3 P2 P1 P0
C1 = G0 + P0 C0
C2 = G1 + P1 G0 + P1 P0 C0

## Slide 43: Carry-select adder
4-Bit Adder [3:0]
C0
C4
4-bit adder [7:4]
1
C8
0
C8
five 2:1 mux
0
1
0
1
0
1
0
1
adder low
adder high
0
1
4-bit adder [7:4]
C8
S7
S6
S5
S4
S3
S2
S1
S0
Redundant hardware to make carry calculation go faster
  compute two high-order sums in parallel while waiting for carry-in
  one assuming carry-in is 0 and another assuming carry-in is 1
  select correct result once carry-in is finally computed

## Slide 44: Arithmetic logic unit design specification
logical and arithmetic operations not all operations appear useful, but "fall out" of internal logic
S1 0 0 1 1
S0 0 1 0 1
Function Fi = Ai Fi = not Ai Fi = Ai xor Bi Fi = Ai xnor Bi
Comment input Ai transferred to output complement of Ai transferred to output compute XOR of Ai, Bi compute XNOR of Ai, Bi
M = 0, logical bitwise operations
M = 1, C0 = 0, arithmetic operations
0 0 1 1
0 1 0 1
F = A F = not A F = A plus B F = (not A) plus B
input A passed to output complement of A passed to output sum of A and B sum of B and complement of A
M = 1, C0 = 1, arithmetic operations
0 0 1 1
0 1 0 1
F = A plus 1 F = (not A) plus 1 F = A plus B plus 1 F = (not A) plus B plus 1
increment A twos complement of A increment sum of A and B B minus A

## Slide 45: Arithmetic logic unit design (cont’d)
M 0 1 1
S1 0 0 1 1 0 0 1 1 0 0 1 1
S0 0 1 0 1 0 1 0 1 0 1 0 1
Ci X X X X X X X X X X X X 0 0 0 0 0 0 0 0 0 0 0 0 1 1 1 1 1 1 1 1 1 1 1 1
Ai 0 1 0 1 0 0 1 1 0 0 1 1 0 1 0 1 0 0 1 1 0 0 1 1 0 1 0 1 0 0 1 1 0 0 1 1
Bi X X X X 0 1 0 1 0 1 0 1 X X X X 0 1 0 1 0 1 0 1 X X X X 0 1 0 1 0 1 0 1
Fi 0 1 1 0 0 1 1 0 1 0 0 1 0 1 1 0 0 1 1 0 1 0 0 1 1 0 0 1 1 0 0 1 0 1 1 0
Ci+1 X X X X X X X X X X X X X X X X 0 0 0 1 0 1 0 0 0 1 1 0 0 1 1 1 1 1 0 1
Sample ALU – truth table

## Slide 46: Arithmetic logic unit design (cont’d)
12 gates
\S1
\Bi
[35]
[35]
M
M
M
S1
Bi
[33]
[33]
[33]
[33]
S0
Ai
[30]
[30]
[30]
[30]
[30]
Ci
Ci
Ci
Ci
Co
\Co
\Co
\Co
\[30]
\[35]
Fi
Sample ALU – multi-level discrete gate logic implementation

## Slide 47: Arithmetic logic unit design (cont’d)
Bi
S1 Ai
S0
Ci
M
Fi
Ci+1
X1
X2
X3
A1 A2
A3 A4
O1
first-level gates
  use S0 to complement Ai S0 = 0 causes gate X1 to pass Ai S0 = 1 causes gate X1 to pass Ai'
  use S1 to block Bi S1 = 0 causes gate A1 to make Bi go forward as 0 (don't want Bi for operations with just A) S1 = 1 causes gate A1 to pass Bi
  use M to block Ci M = 0 causes gate A2 to make Ci go forward as 0 (don't want Ci for logical operations) M = 1 causes gate A2 to pass Ci
other gates
  for M=0 (logical operations, Ci is ignored)
    Fi = S1 Bi xor (S0 xor Ai)
    = S1'S0' ( Ai ) + S1'S0 ( Ai' ) + S1 S0' ( Ai Bi' + Ai' Bi ) + S1 S0 ( Ai' Bi' + Ai Bi )
  for M=1 (arithmetic operations)
    Fi = S1 Bi xor ( ( S0 xor Ai ) xor Ci ) =
    Ci+1 = Ci (S0 xor Ai) + S1 Bi ( (S0 xor Ai) xor Ci ) =
    just a full adder with inputs S0 xor Ai, S1 Bi, and Ci
Sample ALU – clever multi-level implementation

## Slide 48: Summary for examples of combinational logic
Combinational logic design process
  formalize problem: encodings, truth-table, equations
  choose implementation technology (ROM, PAL, PLA, discrete gates)
  implement by following the design procedure for that technology
Binary number representation
  positive numbers the same
  difference is in how negative numbers are represented
  2s complement easiest to handle: one representation for zero, slightly complicated complementation, simple addition
Circuits for binary addition
  basic half-adder and full-adder
  carry lookahead logic
  carry-select
ALU Design
  specification, implementation