## Slide 1: Patch Descriptors 1
ECE P 596
Linda Shapiro

## Slide 2
How can we find corresponding points?

## Slide 3: How can we find correspondences?

## Slide 4
How do we describe an image patch?

## Slide 5
How do we describe an image patch?
Patches with similar content should have similar descriptors.

## Slide 6: Raw patches as local descriptors
The simplest way to describe the neighborhood around an interest point is to write down the list of intensities to form a feature vector.
But this is very sensitive to even small shifts, rotations.

## Slide 7: SIFT descriptor
Full version
  Divide the 16x16 window into a 4x4 grid of cells (2x2 case shown below)
  Compute an orientation histogram for each cell
  16 cells * 8 orientations = 128 dimensional descriptor
Adapted from slide by David Lowe

## Slide 8: SIFT descriptor
Full version
  Divide the 16x16 window into a 4x4 grid of cells
  Compute an orientation histogram for each cell
  16 cells * 8 orientations = 128 dimensional descriptor
8 8 . . . 8

## Slide 9
0.37
0.79
0.97
0.98
0.97
0.91
0.98
0.79
0.73
0.90
0.75
0.31
0.45
0.45
0.04
0.08
by Yao Lu
Numeric Example

## Slide 10
L(x-1,y-1)
L(x,y-1)
L(x+1,y-1)
0.98
0.97
0.91
0.98
L(x+1,y)
L(x+1,y+1)
0.90
0.75
L(x,y+1)
0.45
L(x-1,y+1)
L(x-1,y)
magnitude(x,y)=
(x,y)=
L(x,y)
(x,y)
by Yao Lu

## Slide 11
Orientations in each of
the 16 pixels of the cell
The orientations all
ended up in two bins:
11 in one bin, 5 in the
other. (rough count)
5 11 0 0 0 0 0 0

## Slide 12: SIFT descriptor
Full version
  Start with a 16x16 window (256 pixels)
  Divide the 16x16 window into a 4x4 grid of cells (16 cells)
  Compute an orientation histogram for each cell
  16 cells * 8 orientations = 128 dimensional descriptor
  Threshold normalize the descriptor:
Adapted from slide by David Lowe
0.2
such that:

## Slide 13: Properties of SIFT
Extraordinarily robust matching technique
  Can handle changes in viewpoint
    Up to about 30 degree out of plane rotation
  Can handle significant changes in illumination
    Sometimes even day vs. night (below)
  Fast and efficient—can run in real time
  Various code available
    http://www.cs.ubc.ca/~lowe/keypoints/

## Slide 14: Example
NASA Mars Rover images
with SIFT feature matches Figure by Noah Snavely

## Slide 15: Example: Object Recognition
Lowe, IJCV04
SIFT is extremely powerful for object instance recognition, especially for well-textured objects

## Slide 16: Example: Google Goggle

## Slide 17: panorama?
We need to match (align) images

## Slide 18: Matching with Features
Detect feature points in both images

## Slide 19: Matching with Features
Detect feature points in both images
Find corresponding pairs

## Slide 20: Matching with Features
Detect feature points in both images
Find corresponding pairs
Use these matching pairs to align images - the required mapping is called a homography.

## Slide 21: Automatic mosaicing

## Slide 22: Recognition of specific objects, scenes
Rothganger et al. 2003
Lowe 2002
Schmid and Mohr 1997
Sivic and Zisserman, 2003
Kristen Grauman

## Slide 23: Example: 3D Reconstructions
Photosynth (also called Photo Tourism) developed at UW by Noah Snavely, Steve Seitz, Rick Szeliski and others
http://www.youtube.com/watch?v=p16frKJLVi0
Building Rome in a day, developed at UW by Sameer Agarwal, Noah Snavely, Steve Seitz and others
http://www.youtube.com/watch?v=kxtQqYLRaSQ&feature=player_embedded

## Slide 24: When does the SIFT descriptor fail?
Patches SIFT thought were the same but aren’t:

## Slide 25: Other methods: Daisy
SIFT
Daisy
Picking the best DAISY, S. Winder, G. Hua, M. Brown, CVPR 09
Circular gradient binning

## Slide 26: Other methods: SURF
For computational efficiency only compute gradient histogram with 4 bins:
SURF: Speeded Up Robust Features
Herbert Bay, Tinne Tuytelaars, and Luc Van Gool, ECCV 2006

## Slide 27: Other methods: BRIEF
Daisy
BRIEF: binary robust independent elementary features, Calonder, V Lepetit, C Strecha, ECCV 2010
Randomly sample pair of pixels a and b.
1 if a > b, else 0. Store binary vector.
a
b
011000111000...

## Slide 28: Descriptors and Matching
The SIFT descriptor and the various variants are used to describe an image patch, so that we can match two image patches.
In addition to the descriptors, we need a distance measure to calculate how different the two patches are?
?

## Slide 29: Feature distance
How to define the difference between two features f1, f2?
  Simple approach is SSD(f1, f2)
    sum of square differences between entries of the two descriptors
    i
    But it can give good scores to very ambiguous (bad) matches
I1
I2
f1
f2
Σ (f1i – f2i)2

## Slide 30: Feature distance in practice
How to define the difference between two features f1, f2?
  Better approach: ratio distance = SSD(f1, f2) / SSD(f1, f2’)
    f2 is best SSD match to f1 in I2
    f2’ is 2nd best SSD match to f1 in I2
    gives large values (~1) for ambiguous matches WHY?
I1
I2
f1
f2
f2'

## Slide 31: Eliminating more bad matches
Throw out features with distance > threshold
  How to choose the threshold?
50
75
200
feature distance
false match
true match

## Slide 32: True/false positives
The distance threshold affects performance
  True positives = # of detected matches that are correct
    Suppose we want to maximize these—how to choose threshold?
  False positives = # of detected matches that are incorrect
    Suppose we want to minimize these—how to choose threshold?
50
75
200
feature distance
false match
true match

## Slide 33: Finale
Describing images or image patches is very important for matching and recognition
The SIFT descriptor was invented in 1999 and is still very heavily used.
Other descriptors are also available, some much simpler, but less powerful.