## Slide 1: Efficient and Accurate Mitosis Detection: A Lightweight RCNN Approach
Yuguang Li2, Ezgi Mercan1
Stevan Knezevitch3,
Joann G. Elmore4, Linda G. Shapiro1
1 Paul G. Allen School of Computer Science and Engineering, University of Washington 2 Department of Electrical Engineering, University of Washington 3 Pathology Associates 4 Department of Medicine, University of Washington

## Slide 2: Medical Diagnosis of Cancer
tissue specimen
H&E staining
glass slide
whole slide imaging
light microscope

## Slide 3: Mitotic Figures
Terminology:
Whole Image Slides
Histopathological Images
Tissue Staining
Cell
Mitosis
Scale x10
Whole Slide
Scale x40
Region of Interest
Region of Tumor

## Slide 4: Objective: Counting Mitotic Figures
Challenges:
Small objects with a large variety of shape configurations & texture variation
Low frequency
Similarity with other types of nuclei
Mitosis
Non-Mitosis

## Slide 5: Datasets
ICPR 2012
Training: 15 images & 100 mitoses
Test: 35 images & 200 mitoses
Image size is 2084 x 2084 pixel
ICPR 2014
Training 1200 images
Test: 496 images
Image size is 1539 x 1539 pixel
Probabilistic mitotic figure labels
Images from a large number of different biopsies

## Slide 6: Region-based Convolutional Neural Network

## Slide 7: Motivation for the RCNN Work
Training Efficiency
 | ICPR12 Initial Set | ICPR12 Augmented Set | 
 | NVIDIA K40 | NVIDIA K40 | CPU
10-layer CNN | 40 min. | 8 hrs. | 20hrs
12-layer CNN | 2 hrs. | 12 hrs. | 45hrs
Random forest classifier is trained in less than 1 minute with extracted features on a CPU machine.
Testing Efficiency
CNN(5-pixel scanning interval)
Image tested with 8 rotations:
24min per image with CPU
CNN (Caffe library)
CNN + feature-based Method
Lots of unnecessary scans!!!

## Slide 8: Mitosis Detection Pipeline
Stage 1: The CCE extracts
pixel-wise features at
different scales and
classifies each pixel as
possibly mitosis or not
Stage 2: The FCE uses a
CNN to check a fixed size
region centered at each
positive pixel to decide if
it is a possible mitosis.
Stage 3: The FMP uses
the same CNN to check
multiple pixels and also
multiple rotations.

## Slide 9: Stage 1: Coarse Candidate Extractor
37 multi-scale features
  Color (pixel values in Gaussian-smoothed color images)
  Edge (Gaussian Gradient Magnitude, Gaussian Gradient Magnitude, Laplacian of Gaussian and Difference of Gaussian)
  Texture (Structure Tensor Eigenvalues and Hessian of Gaussian Eigenvalues)
Feature selection to reduce 37 to 10.
Random forest classifier with six trees uses the 10 features to label pixels as mitotic candidate or not.

## Slide 10: Selected 10 Features

## Slide 11: Stage 2: Fine Candidate Extractor
Uses a CNN model trained using the ground truth training data provided by the organizers of the ICPR12 and ICPR 14 contests.
We color normalized it according to a color transfer method described in Reinhard et al. 2001.
Each pixel of each training image is labeled a mitosis if it is a pixel of a mitotic region and within 8 µm of the centroid.
For ICPR14 data, which is probabilistic, only mitotic regions with probability > 0.6 were used.
The two stage sampling techniques from Ciresan et al 2013 were used to build the final training image sample set.

## Slide 12: CNN Structure
Testing method: Sliding Window
RGB Patch Input
CNN Classifier
Probability
Probability Map
Original Image
Layer | Type | Neurons | Filter Size
0 | Input | 3M x 101 x 101 | --
1 | Conv | 16M x 100 x 100 | 2 x 2
2 | MaxPool | 16M x 50 x 50 | 2 x 2
3 | Conv | 16M x 48 x 48 | 3 x 3
4 | MaxPool | 16M x 24 x 24 | 2 x 2
5 | Conv | 16M x 22 x 22 | 3 x 3
6 | MaxPool | 16M x 11 x 11 | 2 x 2
7 | Conv | 16M x 10 x 10 | 2 x 2
8 | MaxPool | 16M x 5 x 5 | 2 x 2
9 | Conv | 16M x 4 x 4 | 2 x 2
10 | MaxPool | 16M x 2 x 2 | 2 x 2
11 | FullyConn | 100 | 1 x 1
12 | FullyConn | 2 | 1 x 1
12-layer CNN Model

## Slide 13: Training the CNN
Objective: Train a classifier to detect the mitosis at the center of a patch.
Challenges:
Very few positive samples: Only 200 mitoses in training set.
Trained classifier needs to be rotational and shift invariant.
Solutions:
We used random rotation, shift and mirroring to augmented the positive training samples.
In the first stage, we are using 66000 mitosis and 66000 non-mitosis patches in training samples.
Non-mitosis samples are randomly selected from the non-mitosis areas.
Augmented Training Samples:
Test samples:

## Slide 14: Training the CNN
Step 1: Initial training set
Positive Samples: Apply rotations and shifts on 200 mitosis.
Negative Samples: Randomly sampled from the non-mitosis pixels.
Step 2: Augmented training set
Positive Samples: Same samples as above
Negative Samples: Use the probability of false positive samples from last step as sampling probabilities to create a lot more difficult samples.
66000 Mitosis
66000 Non-mitosis
66000 Mitosis
1million Non-mitosis
Have the classifier learn difficult samples.
Sampling Probability Map

## Slide 15: Testing process
Threshold Values | Precision | Recall | F-Score
0.5 | 0.69 | 0.86 | 0.77
0.6 | 0.73 | 0.84 | 0.77
0.7 | 0.78 | 0.79 | 0.78
0.8 | 0.84 | 0.73 | 0.78
0.9 | 0.87 | 0.70 | 0.78
 | Precision | Recall | F-Score
Single Direction | 0.78 | 0.74 | 0.76
8-direction Average | 0.78 | 0.79 | 0.78
Ciresan et al | 0.88 | 0.70 | 0.78
Original Input Image
Rotate 90° with/ without mirroring (8 images)
8 CNN predictions
Average Probability
Final Label from thresholding
Accuracy from CNN Model with/ without 8 direction Average
Accuracy from CNN Model with different thresholds

## Slide 16: Stage 3: Final Mitosis Predictor
Inputs the binary image produced by the FCE and uses the same trained CNN, but in a sequence of scans of multiple different pixels of the input image.
Each pixel that passes Stage 2 leads to a detailed search of a region around it for evidence of a mitotic figure.
A spiral scan path carries out this detailed search.
Pixels that pass Stage 2 become the centers for the first scan in Stage 3 at an intermediate threshold.
If a pixel in the first scan passes, the system goes into a finer scanning mode at a final threshold.

## Slide 17: Scan path of final mitosis classifier

## Slide 18: Results on ICPR 2012 and 2014 Datasets: Accuracy

## Slide 19: Results on ICPR 2012 and 2014 Datasets: Efficiency
Performance comparison between Stages 2 and 3 of our pipeline and the fine discrimination model of Chen’s pipeline (Chen et al., 2016) for inference on 4Mpixels HPF images from the ICPR12 dataset.

## Slide 20: Conclusions
We proposed a hybrid mitosis detection pipeline which combine efficient handcrafted feature-based pixel classifiers and CNNs in multi-stage pipelines.
Compared to the state-of-the-art methods, our approach reduced the computation amounts and hardware requirements, which makes it more practical in clinical applications.