## Slide 1: 3D Localization for Sub-Centimeter Sized Devices
Rajalakshmi Nandakumar,
Vikram Iyer, Shyam Gollakota

## Slide 2
Recent localization work on improving accuracy
Do not meet the needs of small IoT devices
[1] D. Vasisht, et al. NSDI’16
[2] M. Kotaru, et al. SIGCOMM’15
[3] L. Yang, et al. MobiCom ’14
[4] J. Wang, et al. SIGCOMM ’14
[5] B. Kempke, IPSN’16.
[6] L. Chuo, Mobicom’17.
UWB

## Slide 3
No technology to track mobile IoT devices through
walls on button cell batteries

## Slide 4
Bluetooth
Battery life with radios is very limited
Battery life (months)
1% duty cycle
6
4
2
0
BLE
(CC2640)
LoRa
(SX1276)
UWB
(DW1000)
Wi-Fi
(CC3100)
Coin cell (CR2032)
2x Button cell
(LR64)

## Slide 5
Existing tech: Trade off between size and battery life
44.5 mm
5.8 mm

## Slide 6
First uW localization system for mobile IoT devices that works across multiple rooms
Sub centimeter programmable microcontroller based prototype that can be integrated with sensors
Real world deployments across 5 homes and a hospital
uLocate

## Slide 7
uLocate
Capabilities
Power 93 uW
Range 60 m
Accuracy 50 cm @ 30 m
Latency < 70 ms
Lifetime >5 years @ 1 %

## Slide 8
Outline
Long range communication at low power for sub-centimeter devices
Phase extraction algorithm below noise floor
Addressing multipath to compute 3D location

## Slide 9
How do we communicate at long ranges?
Naïve Solution: Use LoRa backscatter[7]
Single tone
from AP
Backscattered
chirp
Coding requires large FPGAs  size and power too high
[7] V. Talla, et al. LoRa Backscatter: Enabling The Vision of Ubiquitous Connectivity IMWUT, 2017
f
f
45 mm

## Slide 10
Key Idea: Outsource coding to the access point
Architecture enables small, low power, long range communication
f
Chirp from AP
AP
TX
RX
Backscattered chirp
f
f
IoT Device
Oscillator

## Slide 11
Outline
Long range communication at low power for sub-centeimeter devices
Phase extraction algorithm below noise floor
Addressing multipath to compute 3D location

## Slide 12
Why do we need the phase?
Channel phase
∝ distance
Need to find exactly when chirp arrives
Signal is below the noise floor
Microcontroller isn’t synchronized
Extract channel phase from chirp phase
Wireless Channel
Extracting Phase

## Slide 13
How do we decode chirps below the noise floor?
FFT Bin
Amplitude
FFT
Solution: Use correlation to get coding gain
Carrier frequency offset (CFO) also shifts the FFT peak
Use shift in FFT peak to find start time
x
Upchirp
Downchirp

## Slide 14
How do we correct for CFO?
x
Upchirp
Downchirp
FFT Bin
Amplitude
f1
f0
fn
fn+1
FFT
CFO
Key Idea: CFO stays constant when shifting chirp

## Slide 15
How do we extract the channel phase?
Solve for Φchan  solve for d
+ +

## Slide 16
Outline
Long range communication at low power for sub-centeimeter devices
Phase extraction algorithm below noise floor
Addressing multipath to compute 3D location

## Slide 17
How do we deal with multipath?
Solution: Design multi-band backscatter system
Problem: 500 kHz chirp  572 frequencies x 7 ms > 4 s
26 MHz
80 MHz
180 MHz
Frequency
2.4 GHz
900
MHz
5.2 GHz
5.8 GHz

## Slide 18
Faster solution: Dynamic frequency selection
Leverage path loss to only query the frequencies we need
Maximize the difference between queried frequencies
Perform queries in parallel
Frequency
2.4 GHz
900
MHz
5.2 GHz
5.8 GHz

## Slide 19
How do we use this to help with multipath?
Take IFFT of queries and threshold to pick the closest reflection
How do we know when to stop?
 Only query when |Loc1-Loc2|> ε
How do we get 3D location?
 Nonlinear least squares to intersect 3 estimates
Putting it all together: Solving for location
> ε
Loc1
Loc2
Estimate

## Slide 20
55
45
35
25
15
5
What is our localization accuracy?
Error <15 cm in next room, < 50 cm through down the hall
Office Deployment
3D Location Error (cm)
20 m
2 3 4 5 6 7
Location

## Slide 21
AP
60 m
3D Location Error (cm)
What is our localization accuracy?
Open field experiments
160
120
80
40
0
10 20 30 40 50 60
Range (m)
Localization error: 25 cm @ 20 m
78 cm @ 40 m

## Slide 22
0 10 20 30 40 50 60
Range (m)
What is the latency for localizing?
Latency <70 ms across whole range
Number of Frequencies
28
24
20
16
12
8
Latency (ms)
65
55
45
35
25
Latency

## Slide 23
What is the power consumption?
Coin cell (CR2032)
2x Button cell
(LR64)
10
8
6
4
2
0
Battery Life (Years)
Button cell lifetime
@ 1% duty cycle >5 yrs
Microcontroller
@1% duty cycle

## Slide 24
Real world deployment: Homes
Apartments <30 cm, Multi-story homes < 1.2m
Home 1 Home 2 Home 3 Home 4 Home5
0 20 40 60 80 100 120 140
Localization Error (cm)
1
0.8
0.6
0.4
0.2
0
CDF

## Slide 25
Real world deployment: Hospital surgery wing
Mean error: 35.1 cm, Max error: 70 cm
20 m

## Slide 26
First uW localization system for mobile IoT devices that works across multiple rooms
Sub-centimeter programmable microcontroller based prototype that can be integrated with sensors
Real world deployments across 5 homes and a hospital
Conclusion